Telephone Shilpa Sangstha Limited

Tongi, Gazipur

(A State Own Public Limited Company)

BIDDING DOCUMENT

FOR

"Supply, Installation, Testing and Commissioning of  OLT & ONU in SKD condition on Turn-key Basis"

Book - 2 (Two)

TECHNICAL SPECIFICATION

TENDER NO. TSS/FP/OLT&ONU/2010/01

# DATED : 24/03/2010

TENDER DOCUMENT FOR MULTI SERVICE ACCESS NETWORK THROUGH OPTICAL FIBER CABLE

BOOK TWO

TABLE OF CONTENTS

CHAPTER 1...............................................................................................................................................................3

SPECIAL INFORMATION AND INSTRUCTION TO BIDDERS                                                                          3

CHAPTER 2................................................................................................................................................................8

SCOPE OF WORKS                                                                                                                                                 8

CHAPTER 3...............................................................................................................................................................20

ENVIRONMENTAL AND OTHER REQUIREMENTS                                                                                          20

CHAPTER 4...............................................................................................................................................................21

REQUIREMENTS OF MULTI SERVICE ACCESS NETWORK EQUIPMENT                                                    21

CHAPTER 5...............................................................................................................................................................28

REQUIREMENTS OF  THE OPERATION AND MAINTENANCE FACILITIES                                                 28

CHAPTER 6...............................................................................................................................................................35

TECHNICAL REQUIREMENT FOR OUTSIDE PLANT (OSP) SYSTEM                                                            35

CHAPTER 7...............................................................................................................................................................54

REQUIREMENTS OF  THE ANCILLARY FACILITIES                                                                                       54

CHAPTER 8...............................................................................................................................................................58

CRITERIA FOR EVALUATION OF BIDS : EVALUATION OF SUBSTANTIAL RESPONSIVENESS             58

CHAPTER 9.............................................................................................................................................62

CRITERIA FOR EVALUATION OF BIDS :                                                                                           62

CHAPTER 10.............................................................................................................................................................65

MECHANISM FOR AWARDING THE CONTRACT                                                                                            65

ANNEX 1.1............................................................................................................................................ .67

CAPACITY REQUIREMENT OF OLT                                                                                                   67

ANNEX 1.2...............................................................................................................................................68

CAPACITY REQUIREMENT OF ONU                                                                                                   68

ANNEX 1.3................................................................................................................................................................70

CAPACITY REQUIREMENT OF MDF PATCH PANEL                                                                                       70

ANNEX-1.4 .............................................................................................................................................71

CAPACITY REQUIREMENT OF ODF                                                                                                    71

FORM A....................................................................................................................................................................72

SUMMARY PRICE OF THE BID                                                                                           72

FORM B.1 .................................................................................................................................................................73

SUMMARY PRICE FOR OLT EQUIPMENT                                                                                                          73

FORM B.2 .................................................................................................................................................................74

SUMMARY PRICE FOR ONU EQUIPMENT                                                                                                          74

FORM B.3 ...............................................................................................................................................75

SUMMARY PRICE FOR MDF                                                                                                                  75

FORM B.4 .............................................................................................................................................. .76

SUMMARY PRICE FOR ODF                                                                                            76

FORM B.5 .................................................................................................................................................................77

SUMMARY PRICE FOR OTHER EQUIPMENT                                                                                                      77

FORM B.6 .................................................................................................................................................................78

SUMMARY PRICE FOR OTHER SERVICES

FORM B.7 ..................................................................................................................................................79

SUMMARY PRICE FOR OSP                                                                                                                      79

FORM C.1 ...................................................................................................................................................83

83

Detail BoQ for OLT

FORM C.2 ................................................................................................................................................................84

Detail BoQ for ONU

84

FORM C.3 ................................................................................................................................................................85

Detail BoQ for MDF

85

FORM C.4 ................................................................................................................................................................86

Detail BoQ for ODF

86

F

ORM C.5 ................................................................................................................................................................87

DETAIL BOQ FOR OTHER EQUIPMENT

87

FORM C.6 ................................................................................................................................................................88

DETAIL BOQ FOR OTHER SERVICES

88

FORM D....................................................................................................................................................................89

DETAIL BOQ FOR MAINTENANCE SPARES FOR BUFFER STOCK

89

FORM E ....................................................................................................................................................................90

QUOTATION FOR FUTURE ORDER

90

FORM F....................................................................................................................................................................91

SUMMARY OF THE BID EQUIPMENT

91

Book Two

Chapter 1

SPECIAL INFORMATION AND INSTRUCTION TO BIDDERS

1.1.  The bid shall be of “one Envelop” system as per “The Public Procurement Regulation 2006”.

1.2.  The submitted Envelop containing the bid shall have “three parts” in three separate folder. The

first part is Mandatory Documents, the second is Detail Technical Documents and the third

is Financial Documents. Any disagreement shall result in rejection of the bid and shall not

be considered for evaluation by TEC.

1.3.  The Bidders “Mandatory Documents” folder shall contain the following documents in each

set and a total of four (4) sets (one original, 3 photocopy) shall be submitted.

1.3.1.  Tender Document Purchase Receipt (original in one set and copies in other sets)

1.3.2.  Forwarding of the Bid (as per “Annex A" attached in Book 1, duly filled up and properly

signed.)

1.3.3.  Bid Security / Bank Guarantee (as per “Annex B” attached in Book 1, duly filled up and

properly signed).

1.3.4.  The Bond for Spares (as per “Annex D.1.” attached in Book 1, duly filled up and properly

signed).

1.3.5.  The Bond for Expansion (as per “Annex D.2.” attached Book 1, duly filled up and properly

signed).

1.3.6.  The list of attached certificates (as per “Annex F” attached in Book 1, duly filled up and

properly signed).

1.3.7.  A “Declaration on Observance of Ethics” (as per “Annex G” attached in Book 1, duly filled up

and properly signed).

1.3.8.  A “Declaration of Joint Liability” (as per “Annex H” attached in Book 1, duly filled up and

properly signed) [applicable only if the bid is submitted by a Joint Venture

Company/Consortium]

1.3.9.  The Annex 1.1. to 1.4., attached in Book Two, duly filled up .

1.3.10. Bid Summary (as per format shown in “Form F” attached in Book Two, duly filled up).

1.3.11. Principal’s Letter of Authority (if the bid is submitted by an entity other than principal).

1.3.12. The letter of authority of the manufacturer of  Multi Service Access Network (Optical Line

Termination -OLT & Optical Network Unit-ONU )to participate in this bid (if the bidder is

not manufacturer of the equipment under the bid and for applicable equipment only).

1.3.13. Guarantee certificates from the manufacturer (On Manufacturer’s letterhead) regarding

continuous supply of spare parts of OLT /ONU  for 7 (Seven) years from the date of issuance

of  FAC.

1.4     The second part titled “Detail Technical Documents” shall contain

1.4.1  Documentary Evidences to Establish Equipment’s Performance

1.4.1.1  Certificates in support of successful running of commercial Multi Service Access

network containing the offered brand OLT & ONU in at least 4 (Four) countries. In

each country, the deployed network must have at least 30,000 subscriber lines

(Telephone, ADSL, FE ) after 2003. The certificates must be from the national

telecom/network operator.

1.4.1.2  If any bidder fails to submit certificate(s) required as per Clause-1.4.1.1, the bid shall

be treated as “Substantially Non-responsive” and shall not be taken for further

evaluation.

1.4.2  Documentary Evidence Establishing Bidder’s Experience

1.4.2.1 The bidder must provide a certificate from the relevant telecom authority which should state

that he has successfully installed and commissioned at least one telecom project on turn-key

basis outside its country of origin. Failure to provide such certificate shall be treated as

“material deviation”.

1.4.2.2 If the bidder has completed or is working to complete telecom project(s) in Bangladesh within

last  5(five) years, the bidder must submit a statement mentioning the name of the project(s)

with at  least (but not limited to) the following information for the purpose of post qualification;

i)  Effective date of contract

ii)   Project completion period as per contract

iii)  Status of the project (whether completed or running)

a)  If completed, when.

b)  If running project, then approximate percentage of works completed and expected

date of completion.

iv)  Other related information if any

If any bidder fails to give such statement, the bid shall be treated as “Substantially Non-

responsive” and shall not be taken for further evaluation.

1.4.3  The following documents; one soft copy provided in CD (in MS office & PDF format) and 4

(four) hard copies, of which at least two copies shall be in original.

1.4.3.1 Brochure/ Catalog of the Manufacturer, showing model name, country of origin description and

capacities etc., for OLT, ONU, and NMS. Downloaded documents from web site (address must

be given) shall be acceptable provided that the documents contain the required information.

1.4.3.2 Explanation of Redundancy (whether 1 + 1 or N + 1) of various core elements such as control

processors, back-plane, storage devices, power supply etc.

1.4.3.3 A “Clause by Clause Compliance Schedule” to all the clauses and sub-clauses of the Tender

Document. The schedule shall prepare as per format shown in Book 1 (Annex C) of tender

document.

1.4.3.4 The Tender document duly signed (in original) and stamped in every page by an authorized

representative of the bidder.

1.4.3.5 If the bid is through a local agent, then, Local Agent’s Trade License (updated for current

year).

1.4.3.6 Site-wise break-down of the DC Power consumption (in Ampere) of all OLT at the present

equipped capacity.

1.4.3.7 DC Power requirement (in Ampere) for all the ONU for present capacity along with capacity of

proposed rectifier and  battery .

1.4.3.8 Brochure/ Catalog of the Manufacturer, showing model name, country of origin description and

capacities etc., for minor items namely Rectifier, Battery. Downloaded documents from web

site (address must be given) shall be acceptable provided that the documents contain the

required information.

1.5  If a bidder fails to give any document as per requirement stated in Clause 1.4.3.1 to 1.4.3.2

above, the submitted bid of the bidder shall be treated as "Substantially Non-Responsive".

1.6  Bidder who will not give any document as per requirement stated in Clause 1.4.3.3 to 1.4.3.5,

the bid shall earn penalty point equivalent to a "Material Deviation" for each of such absent

document.

1.7  Bidder who will not give any document as per requirement stated in Clause 1.4.3.6. to 1.4.3.8

above, the bid shall earn penalty point equivalent to a "Major Deviation" for each of such

absent document.

1.8  The third part i.e. “Financial Documents” of the Bidder shall include the following filled up

Forms attached with Book 2 :

1.8.1  Summary of the Bid Price as per “Form A.”

1.8.2  Summary Prices for all equipments/items/services as per format shown in "Form B”s.

1.8.3  Detail BoQ for all equipments/items/services as per format shown in "Form C”s (up to the most

detailed component/element level desired by the bidder).

1.8.4  Detail BoQ for Maintenance Spares for buffer stock, as per format shown in “Form D”.

1.8.5  Pricing Technique for Future Order, as per format shown in "Form E".

1.9  If for any bidder, its bid does not contain all required documents listed in 1.8.1. to 1.8.5 above,

the bid shall be treated as “Substantially Non-Responsive”.

1.10  The documents listed in item 1.4 shall preferably be provided separately in separate Chapters of

the technical document. But co-related items may be merged together or included in one single

chapter. All the Chapters must be marked and numbered clearly and a list of contents must be

provided on top of the technical document.

1.11  Regarding Documents/Certificates, the Bidder should note the following that:

1.11.1 The Documents/Certificates shall be in English or originally in any other language

accompanied by “authorized translation in English”.

1.11.2  Authorized translation in English” shall mean a translated copy in English certified in original

by the authorized official of the diplomatic mission representing Bangladesh in that certificate’s

country of origin.

1.12  The bidder shall provide a list (as per Annex F attached in Book 1 and to be submitted with

Mandatory Documents) of all the certificates. That list shall include detail name and address

with telephone, email & fax numbers of the person signing each of those certificates (including

persons signing the authorized translation in English - where applicable).

1.13  On the day of opening of the tender document, as prescribed by TSS, the bid shall be opened

by the Tender Opening Committee in presence of the Bidders and/or their authorised

representatives (if anybody likes to be present). After opening the bid, the presence of the

necessary documents shall be checked, the total number of certificates, as listed in Annex F

attached in Book 1.

1.14  Based on such examination, observations and information announced at the opening  a

“Tender Opening Sheet (TOS)” shall be prepared. Upon completion of opening of the

tenders, all members of the Tender Opening Committee and the Tenderers or their

representatives who attended the tender opening shall sign the TOS. Upon request copies can

also be made available to the Tenderers.

1.15  On completion of the opening formalities, the tender opening committe shall forward that

statement,along with 2(two) copies of Bid to the "Tender Evaluation Committee" of TSS.

1.16   The TEC  shall follow the guidelines for Evaluation Criteria of Book 2 to evaluate the

bids.

1.17  Eligibility of the Bidder

a)  The bidder must be an International firm engaged in either or both of the following fields

:

i)  Manufacturing of Telecom and/or Data Network equipment; or

ii)  Worldwide marketing, representation and/ or distribution of Telecom Equipment/Data                                                                                                  .                         Network

1.18  The bidder shall also submit necessary documents proving professional and technical

qualifications and competence, financial resources, equipment and other physical facilities,

including after-sales service where appropriate, managerial capability, experience in procuring

object, reputation, and the personnel, to perform the contract. The documents will be used for

“Post-qualification” purpose.

1.19  The bidder shall note that, during submission of the bid, if he does not comply and/or disagree to

any or many specification, terms and/or conditions set forth in this document and/or proposes

any alternate specification, terms and/or conditions; such non-compliance and/or disagreement

and/or alternate specification, terms and/or conditions shall not be binding upon TSS until

and unless such non-compliance and/or specification and/or terms and/or conditions have been

accepted by TSS and has been incorporated in writing in the Purchase Contract and/or any

other document which has been declared as part of the contract.

1.20   bidders/Manufacturers already Black Listed in TSS or BTCL.

Bid of any bidder who is already black listed in TSS or BTCL will be considered as “not eligible”

and will not be considered for evaluation. If any bidder quotes any equipment from any

manufacturer who is already Black Listed in TSS or BTCL, then the bid will be considered as

“not eligible” and will not be considered for evaluation.

Book Two

Chapter 2

SCOPE OF WORKS

2.1 Deleted

2.2  For this purpose, this Tender proposes to procure the following system :

a)  Optical Line Termination Equipment (OLT) having Present capacity requirement as shown

in Annex 1.1

b)  Optical Network Unit (ONU)  of the Present capacity requirement as shown in Annex 1.2

c)  Separate MDF &  ODF at different sites   as shown in Annex 1.3 & 1.4

d)  Network Management System, Other equipment/materials/services.

2.3  Unless otherwise described in the Technical Specifications, the scope of provision shall cover

, supplying, installing, testing, commissioning of equipment and material and its related facilities

on “Turn-Key” basis.

2.4 Deleted

2.5  Detail Technical Specifications of various components of the required system/service are given

in subsequent chapters of this document.

2.6  Maintenance Spares for buffer stock

2.6.1  The Bidder shall supply one separate list for essential “Maintenance Spares” to be maintained

as a central buffer stock by TSS for emergency purposes.

2.6.2  That list must include at least two units of each replaceable item for all equipment covered by

this purchase. Number of units may be more depending upon the size of the node and MTBF of

the critical equipments/components. But, for subscriber line cards (POTS, ADSL, FE card) the

number will be at least 10% (Ten percent) of the total number of line cards quoted in the offer

for the entire network.

2.6.3  The quotation for such list (in Form D) is mandatory and failure to quote shall be regarded as

“non-compliance” and it shall be considered that the bidder proposes to supply any quantity

of spares, as fixed up by TSS during contract negotiation, “free of charge” to TSS.

2.7  Spare parts and consumables used before end of Guarantee Period

All necessary spare parts and consumables, used during installation, testing & commissioning

and operation of the systems, up to the end of Performance Guarantee Period, shall be

supplied by the Bidder at his own cost.

2.8  Spare Parts Guarantee

The Bidder shall provide a separate guarantee (as per format in Annex E.1.of Book 1) to the

effect that, he shall guarantee the flow and availability of all spare parts, software and units without

major design changes for at least 7(Seven) years from “the date of effect” of the Final

Acceptance Certificate (FAC). If, within this period, there is any major design change or

stoppage of production of supplied equipment, the bidder shall bear all the costs related to

provision of alternate solutions.

If the bidder disagrees to the format of the guarantee, as shown in Annex E.1., the bid shall be

considered having “material deviation”

2.9  Expansion Guarantee

The Bidder shall provide a separate guarantee (as per format in Annex E.2.of Book 1) to the

effect that, he shall guarantee the flow and availability of all equipment, materials and services

required for any subsequent expansion of its offered equipment for at least 7(Seven) years from

“the date of effect” of the Final Acceptance Certificate (FAC). If, within this period, there is

any major design change or stoppage of production, the bidder shall bear all the costs related to

provision of alternate solutions.

If the bidder disagrees to the format of the guarantee, as shown in Annex E.2., the bid shall be

considered having “material deviation”

2.10 Maintenance Support

2.10.1  Maintenance Support up to Performance Guarantee Period

i)  The Bidder, at his own cost, shall engage at least 1 (one) Operation and Maintenance

(O&M) Engineer. The Engineer shall be stationed in Dhaka to provide full maintenance

support for all equipment covered by this purchase up to the end of the Performance

Guarantee Period. This support service shall start from the date of cut-over of the first site

covered by this purchase.

ii)  The support Engineer will be fluent in English and will have enough knowledge of the

relevant system to effectively solve all O&M problems; the person must also have at least

3(three) years of prior experience of providing such support in other countries. The bidder shall

be responsible for all types of expenditure to be borne for the manpower, including all types of

transportation.

iii)  The maintenance support service shall cover at least (for 7 years along with) the following

services and if the bidder disagree to this format of the services, the bid shall be considered

having "material deviation".

.

c)  helping maintenance  personnel  of  to solve different software and hardware problems related to

proper O&M of the equipment

d)  identify and remove different bugs in the system's operational software

e)  helping TSS or maintenance personnel to properly maintain relevant databases related to O&M      of the system.

g)  giving regular on-the-job training to maintenance   personnel about different aspects of O&M

h)  advising about different aspects of O&M, system dimensioning, expansion etc.

i)  transfer of technology to TSS or its nominated  organization.

2.11 Performance Guarantee Period

2.11.1  The bidder’s offer shall include an overall “Performance Guarantee Period” for the whole

equipment covered by this purchase. This period shall deem to have started from the cut-over

of the first equipment into commercial service and last for 2(two) calendar years from “the

date of effect” of the last PAC of the contract.

2.11.2   During the period of this Guarantee, the bidder shall offer all material, equipment, services and

Maintenance support as described in relevant clauses for Spare Parts and “Maintenance

Support up to Guarantee Period”.

2.11.3  Bidders refusal to offering of the guarantee specified in this clause shall be treated as “Change

of Substance”.

2.12    Testing

2.12.1  Provisional Acceptance Test (PAT)

i)  Before acceptance of the installed system/ equipment, TSS and  BTCL  representatives shall

jointly carryout, on  Dhaka site, detailed tests of all equipment to ascertain their inter-working ability with relevant equipment of the other manufacturers, working reliability, concurrence to agreed

technical and other specifications, inventory checking of installed equipment etc. Such tests

shall be termed as “Provisional Acceptance Test (PAT)”. Prior to commencement of such

tests, the contractor shall submit a proposed procedure for the PAT to be subsequently passed

by TSS. The PAT will be done by a joint team of TSS & BTCL Engineers and bidder’s Engineers.

ii)  On completion of installation and self-testing of any system/ equipment, the Bidder

shall submit 3(three) copies of self-test results to TSS and offer that system/ equipment for

Provisional Acceptance Test (PAT). TSS shall start along with BTCL such tests within one month after receipt the request. The bidder may, upon agreement by the both party, offer PAT for any part or parts of the total system. Such request for partial PAT may also be asked for by TSS.

iii)  The bidder shall be totally responsible for arrangement of all equipment, fuel for

generators, consumables, test gears and measuring equipment required for the PAT. All costs

for materials and service shall be quoted and failure to quote shall be considered that the bidder

proposes to provide this service totally " free of charge" to TSS.

iv)  The bidder’s engineer shall be liable to make necessary arrangement complete any

kinds of tests requested by PAT members during PAT procedure.

v)  In addition, the bidder has to provide per-diem costs to PAT engineers as per following:

For whole System:

a.     Number of concerned officer/Engineer

:  10 (Ten)

of PAT team

b.   Number of days allowed for per diem charge  :  i. 15 (fifteen) working days per

person for whole OLT/ONU sites

(except NMS site).

:  ii. 4 (four) working days per person

for NMS site

:  iii. 10 (ten) working days per person

for whole OSP site.

c  Per diem charge to PAT members                          :Taka 800/- per day per person

d Other facilities

:  Transportation

However, the bidder shall note that, if necessary, any or all PAT can continue for more than the

above scheduled period; but, in such cases, the bidder shall not be liable to pay per-diem for

those additional days.

2.12.2  Final Acceptance Test (FAT)

i)  After completion of the PAT and cut-over of the system, the Engineers of the Bidder

will take prompt necessary steps to remove all types of faults and replace all types of faulty

equipment at the cost of the supplier. At the end of the “Performance Guarantee Period for

the Contract”, the overall performance of all equipment will be reviewed and this review shall

be termed as “ Final Acceptance Test (FAT)”.

ii)  The review shall include (but not limited to) the required working reliability and

performance standards of the equipment to meet tender specifications, the bidder’s

responsiveness to resolve all shortcomings mentioned in PAT reports and the bidder’s removal

of all pending & outstanding faults or shortages encountered during the Performance

Guarantee Period for the Contract. When this FAT becomes due, the bidder shall make an

Official request for starting of the FAT and TSS or BTCL official shall start the FAT within one month after receipt the request from the bidder.

iii)  The bidder shall be responsible for arrangement of all equipment, consumables, test

gears and measuring equipment required (if any) for such review tests. All costs for materials

and service (if any) shall be quoted and failure to quote shall be considered that the bidder

proposes to provide this service totally " free of charge" to TSS.

2.12.3  Customer Proof of Concept (CPOC)

i)As per government instruction PSI is not needed, accordingly testing at manufacturer’s premises, to be termed as “Customer Proof of Concept (CPOC)”, shall be carried out (on random sampling basis) for all equipment to be supplied under this purchase. The procedure for such CPOC shall have to be approved by TSS before such tests BTCL and TSS will jointly test the equipment to check their conformity with tender, contract and BoQ specifications.

ii)  Bidder shall include in his offer unit price (per person basis) for this CPOC. Failure to

quote shall be considered that the bidder proposes to provide this service totally " free of

charge" to TSS. The details of test program shall be as follows. If the bidder does not agree

to this basic minimum format, its disagreement shall be considered as a “major deviation”.

a)  Number of concerned officers            :  5 (Five)

b)  Number of working days                     :  7 (seven)

c) Per diem charge to concerned officers

:  US$ 100 (One Hundread) per day

(including holidays in

between) per person

d)  Other facilities                                     :  Local Transportation

Standard Accommodation

Medical Services (if required)

Bothway  Air Ticket

2.13 Training

The Bidder shall provide the training to concern user BTCL & TSS Engineering personnel The

curriculum shall be enough to facilitate transfer of technology for planning, designing, expanding and proper operation & maintenance of all the systems covered by this purchases to BTCL&TSS engineering personnel. Bidder shall include in his offer unit price (per person basis) for the Training . Failure to quote shall be considered that the bidder proposes to provide this service totally "free

of charge" to TSS. If the bidder does not agree to this basic minimum format, its disagreement shall be considered as a “major deviation”.

2.13.1Factory Training

Following generic areas should be included in the training program. Actual content of each

item should, however, be customized to match with the architecture and solutions offered by

the bidder.

This course module will cover at least the following broad topics:

Network Essentials and Technologies, Network Design, Hardware Description, Protocols and

Interfaces, Signaling System, Network Management Systems and Tools etc.

The details of this course module is given below:

a)  Number of  concerned officer

: 10 (Ten)

b)  Number of minimum working

: 20 (twenty)

days

c)  Per diem charge to concerned Trainee

:  US$ 100 (Hundread) per day (including

all holidays in between and travel

days) per person

d)  Other facilities                                              : Local Transportation

Standard Accommodation

Medical Services (if required)

Both way  Air Ticket

2.13.2Local Training

The Bidder shall provide practical Equipment based training in Bangladesh at TSS or BTCL

Premises. The details of the local training shall be as follows:

For all equipment:

a) Number of concerned officers                               :  25 (twenty five)

b) Number of minimum working days                      :  20 (twenty)

c) Per diem charge to the Executives                         :  BD Taka 700(Seven hundred)

per day per person for working days

2.14  Certificates to be Issued

2.14.1  Provisional Acceptance Certificate (PAC)

Upon successful completion of the PAT for any, many or all equipment covered by this

purchase, the relevant authority of TSS, shall issue a “Provisional Acceptance Certificate”

(PAC)  for the equipment concerned. The exact breakdown of the purchase into various PAC

components and the number of PACs to be issued shall be agreed upon between TSS and the

bidder during contract negotiation.

2.14.2 Final Acceptance Certificate (FAC)

After completion of the FAT, if and only if, no outstanding issue has been detected, one “Final

Acceptance Certificate” (FAC) covering the entire purchase contract shall be issued by the

relevant authority of user or TSS .

2.14.3 Engineers’ Arrival Certificate (EAC)

During implementation period of the turn-key contract, the bidder shall provide various

services. On arrival of bidder’s engineers for providing a component of such service and on

receipt of written request from the bidder, the concern Office of shall issue “Engineers’

Arrival Certificate (EAC)” for each of such service components. The exact breakdown of the

purchase into various EAC components and the number of EACs to be issued shall be agreed

upon between TSS and the bidder during contract negotiation.

2.14.4  Successful Completion of Services’ Certificate (SCC)

During implementation period of the turn-key contract, the bidder shall provide various time-

bound services like training, maintenance assistance service. On completion of such service

components and on receipt of written request from the bidder, the relevant office of BTCL or TSS shall issue “Successful Completion of Services’ Certificate (SCC)” for each of such service

components. The exact breakdown of the purchase into various SCC components and the

number of SCCs to be issued shall be agreed upon between TSS and the bidder during

contract negotiation.

2.14.5  Arrival of Goods and Materials Certificate

During implementation period of the turn-key contract, the bidder shall ship various

consignments of foreign goods and materials and shall also supply items from local market. On

arrival of such consignments to TSS sites or TSS stores (whichever is applicable) and on

receipt of written request from the bidder, the relevant office of TSS shall issue “Arrival of

Goods and Materials Certificate” for each of such consignments. The number of such

consignments shall be decided by the bidder in accordance with its approved implementation

plan.

2.14.6  Arrival of  Engineers Certificate

During implementation period of the turn-key contract, the bidder shall provide services for

CPOC to be attended by TSS or BTCL Engineers or jointly. On arrival of the Engineers in sites for those tests, the attending Engineers will sign an “Arrival of the Engineers Certificate”. The

number of such certificates shall be decided by the bidder in accordance with its approved

implementation plan.

2.14.7 CPOC Certificate

On successful completion of CPOC jointly by BTCL & TSS engineers, they will sign a "Customer’s of

Proof Concept Test Certificate". The bidder, on its own initiative and cost, shall also conduct such tests for other consignments and shall issue relevant "Customers Proof of Concept Test

Certificate". The number of such certificates shall be decided by the bidder in accordance with

its approved implementation plan.

2.14.8 Certificate for Clearance of Obligations

After the end of Performance Guarantee period, the Contractor shall give a written undertaking

to the relevant Office of TSS to the effect that, in relation to the turn-key execution of

the contract, it has no outstanding dues, liabilities and obligations towards any organization

inside Bangladesh. After receipt of such undertaking and ascertaining the same by proper

verification, the relevant office of TSS shall issue a “Certificate for Clearance of

Obligations” to the contractor. Such a certificate shall be issued only and only if no such

dues, liabilities and obligations are detected.

2.15   Inter-connections

i)  The Bidder shall be responsible for making inter-connection facility (including supply

of all required material, optical fiber cables, connectors at both ends of inter-connecting cable

and related service) between its own system and existing system of BTCL. The Bidder shall

also be responsible for connecting all the concerned equipment with IP backbone. All costs for

materials and service shall be quoted by the bidder in his offer. Failure to quote shall be treated

as “non compliance” and it shall be considered that the bidder proposes to provide this  "free

of charge" to TSS.

ii)  Probable requirements of the connectors, optical fiber cables, cable tray etc. should be

checked during the survey, before the submission of the bid, by the bidder.

2.16  Inter-works with the Existing Systems

The Bidder shall be responsible to ensure that all the system covered by this purchase shall be

able to inter-work with all the existing systems of BTCL. The bidder shall make necessary

survey and shall also be entirely responsible to solve any mismatch, if encountered. The Bidder

shall quote any extra cost, if necessary, and if the bidder fails to quote for this work, he shall

have to complete this work at his own cost. No subsequent additional request for costs for

required interfaces, if any, shall be entertained.

2.17 Installation Material

i)  The Bidder shall quote for all installation material for all of the equipment covered by this

purchase. The Bidder, in his offer shall show, details of required installation material, for

each equipment, per site, separately, to come to a total price for “Installation Material”.

The material shall include all type local material like fuel, power etc necessary to be used

during installation and testing functions.

ii)  These price breakdowns will be used for calculating revised total price if there is any

subsequent change in number  of sites/amount of equipment.

iii) If the bidder fails to give detail breakdown, TSS shall reserve the right to draw its own

conclusions, as and where necessary.

iv) Failure to give detail breakdown shall also be treated as “minor deviation”.

v)  All costs for materials shall be quoted and failure to quote shall be considered that the

bidder proposes to provide these material totally " free of charge" to TSS.

2.18 Installation and Commissioning Services

i)  The Bidder shall be responsible to provide all services related to installation, testing,

commissioning and cut-over services for all equipment covered by this purchase. The

Bidder, in his offer, shall show details of required installation and commissioning services,

for each equipment separately, per site, to come to a total price for “Installation and

Commissioning Services”.

ii)  These price breakdowns will be used for calculating revised total price if there is any

subsequent change in number of sites and/or amount of equipment.

iii) If the bidder fails to give detail breakdown, TSS shall reserve the right to draw its own

conclusions, as and where necessary.

iv) Failure to give detail breakdown shall be treated as “minor deviation”.

v)  All costs for service shall be quoted and failure to quote shall be considered that the bidder

proposes to provide this service totally " free of charge" to TSS.

2.19 Deleted

2.20 Documentation

i)  The Bidder shall supply at least (but not limited to) the following documents before

PAT of each site.

a)  Technical Documentation for all equipment of the Site- 1 set of hard copy and 1 set

in CD; per site.

b)  As-built installation drawings for all equipment : 1 set in CD and 1 set in hard copy;

per site.

c)  Station AC power wiring diagrams : 1 set in CD and 1 set in hard copy per site.

ii)  Detail technical document for NMC: 1 set in CD and 1 set in hard copy.

iii)  Bidder shall include in his offer prices for these Documentation. Failure to quote shall

be treated as “non compliance” and it shall be considered that the bidder proposes to

provide this  "free of charge" to TSS.

2.21  Quotation for additional equipment

If the bidder thinks that any additional equipment, not listed in this document, is needed for

proper implementation and subsequent O&M of the proposed equipment, and also any

equipment mentioned in this document but not in the BoQ form, he shall quote for such

equipment. If any such equipment are not quoted, it shall be deemed that no additional

equipment are necessary for proper implementation and subsequent O&M of the proposed

system. If during implementation and subsequent O&M upto guarantee period, either the bidder

or the purchaser finds that any additional equipment are obligatory for proper implementation

and subsequent O&M of the network, the bidder shall be liable to supply such systems or

equipment, whatever be the required quantity, “free of charge” to TSS.

2.22  Unit Price for Future Orders

i)  The unit prices for all future orders for all equipment and services covered by this purchase

shall be equal to or below the prices quoted in the original contracted offer.

ii)  The Bidder shall quote, with his offer, a detailed ‘Future Order Formula’ separately for

equipment and services in Form E and submit in the Financial Documents.

iii) The new prices as per quoted future order formula shall become effective only for orders

placed after Guarantee Period and up to the life time of all equipments, optical fibers and

services as per BOQ under this purchase.

iv) All parameters of the quoted formulae must be described clearly.

Any disagreement/deviation/non-quotation will be treated as “Change of substance”.

2.23  Possibility of change in Scope of Work and BoQ

The Bidder shall consider that, the size, number, location & city of nodes and other equipment

and subsequently the total BoQ may change, depending upon the actual requirement during

BoQ preparation.

2.24  Omission of any Mandatory Items in the Contracted BoQ.

The bidder shall note that, even if any or many work(s), equipment or service(s) mentioned in

this document as mandatory, is not mentioned in the contract BoQ for any reason, the bidder

shall not be automatically relieved of his responsibility for those items. But if such omission(s)

has (have) previously been agreed, in writing, by TSS, the bidder shall not be

made liable for such omitted items. Such approved omissions, if any, shall have to be put either

into the contract document or into any other document which subsequently is declared as part

of the contract.

2.25  Prevalence of different clauses, chapters and books

If, for any item, the contents of a Clause of any Book contradict with the contents of any other

Clause of the same or other Book of the Tender Document, the prevalence of the Clause shall

be as follows :

a)  In all cases, regulations of Public Procurement Regulation 2006shall prevail over this

Tender Document

b)  In case of different Books, Book Two shall supersede Book 1;

c)  In case of same Book, later page shall supersede previous page

d)  In case of same page, later line will supersede previous age

e)  In case of same Chapter, later Clause shall supersede previous Clause.

2.26  Deviations from  requirements

The bidder shall note that, during submission of the bid, if he does not comply to any or many

requirement and/ or specification and/ or terms or conditions set forth in this document or

proposes any alternate specification and/ or terms and/ or conditions; such non-compliance and/

or alternate specification and/ or terms and/or conditions shall not be binding upon TSS until

and unless such non-compliance and/or terms and/or conditions have been incorporated in

writing in the Purchase Contract.

2.27    The Proposed Network Architecture

The diagram below shows a probable diagram of the network under this project. The OLT will

be installed at Exchange premises providing gateway interface to PSTN, Internet/MPLS and

DDN services. ONU shall be able to provide broadband access (ADSL, ADSL2+ and

G.SHDSL), POTS services, lease-line based access, High Speed internet Service over Optical

Fiber  and DDN requirement for nx 64kbps users. At the initial stage, each ONU will be

connected to OLT in a point-to-point mode (across BTCL’s dark fiber) forming a star topology,

providing Voice & Data services.

The OLT will be connected with

a.  PSTN Exchanges through V 5.2 interfaces

b.  IP/MPLS cloud through Ethernet-based Interface (FE or GE)

c.  Digital Data Network or MUX through Multiple Transparent E1

d.  With ONU through STM-1/STM-4

The ONU will connected with

a.  Telephone Subscriber through copper cable

b.  ADSL+ Telephone User through copper cable

c.  With ISP or HSI user through FE (optical)

d.  Lease Line Subscriber through G.SHDSL

e.  With OLT through STM-1/STM-4

Book Two

Chapter 3

ENVIRONMENTAL AND OTHER REQUIREMENTS

3.1 Climatic Condition

Bidder shall bear the full responsibility to ensure that all of the supplied equipment are capable of

operating in Bangladesh environment without degradation. All of the supplied equipment must work

satisfactorily under the following environmental conditions. Deviation from these values shall be

considered as “major”.

a) Normal Operation

Temperature Range   : 15°C to 35°C

Relative Humidity   : maximum 90 %

b) Short-time Operation (maximum of 06 hrs at a stretch)

Temperature Range   : 5°C to 45°C

Relative Humidity   : maximum 95 %

3.2 Physical Requirement

All components of all of the equipment shall be of highest possible quality design and fully

tropicalized to be used for continuous operation. The metal surface shall either be galvanized or

painted by spray or plated with surface treatment. There shall be no sharp edges or projections. All

power equipment and cables shall be protected with fuses of proper ratings. All equipment racks, sub-

racks and slots shall be clearly marked in English letters for proper recognition. All equipment racks,

sub-racks and slots shall also be provided with proper earthing and shall be protected against any

surge.

3.3 Operating Voltage

The equipment shall operate satisfactorily on the nominal voltage of      -48V DC and within a voltage

range of -43 to -55 Volts DC. Deviation from these values shall be considered as “major”.  If the

server of the NMS runs by DC power, that will be preferable .

3.4  Environment and Power Supply Monitoring

The equipment must provide a complete range of environment and power supply monitoring functions.

It must monitor such parameters such as temperature, smoke, humidity, primary power supply,

batteries status in ONU site. The monitored information must be reported to the operation and

maintenance centre in time.

3.5  Guarantee for Hardware

The Bidder shall guarantee that, the hardware of the system will run without any major  technical

hazard for at least up to 5 (five) years after the date of issuance of FAC. Deviation shall be considered

as “major”.

Book Two

Chapter 4

REQUIREMENTS OF MULTI SERVICE ACCESS NETWORK EQUIPMENT

4.1  General Requirements

Multi Service Access Network Equipment to be installed under this purchase will be of two

types depending on network connectivity and interface/line cards. Optical Line Terminal

(OLT) will be installed at existing Exchange Site of BTCL and Optical Network Unit ( ONU)

will be installed at new places from where service to the subscriber will be provided. The

OLT will be connected with PSTN Exchanges, Internet, Digital Data Network and

Transmission Mux whereas ONU will be connected with telephone, ADSL, Internet and

Leased line & DDN subscriber.

4.1.1  The main components of ONU and OLT  should be the Interface Cards  and optical

transmission unit; besides, its auxiliary functional units include subscriber line test, power

supplies, and environment monitoring module, battery and distribution frame.

4.1.2  All the control card and power supplies should be n+n redundant to avoid any single point of

failure.

4.1.3  The OLT  & ONU Equipment should be capable of  delivering Voice, High Speed Internet, &

Leased Line (point to point) Services.

4.1.4  The OLT & ONU Equipment should be capable of modular expansion. Configuration and

expansion of it should allow great flexibility. The bidder should provide the method of

expansibility in detail to describe what are the cards/module required to meet expandability.

In case of OLT the expansion shall be made only by inserting the interface cards mentioned

in annex 1.1 and in case of ONU the expansion shall be made only by inserting the interface

cards mentioned in annex 1.2.

4.1.5  The OLT / ONU should be manageable from highly efficient NMS with GUI interfaces that

is easy to operate.

4.1.6  The bidder should state the compliance with OLT / ONU technical standards, terminal

management standards, and broadband line test standards.

4.1.7  The OLT/ONU has to be equipped with line testing card to allow test of all types of line cards

from OLT.

4.1.8  The ONU shall support ATM and IP uplinks simultaneously to adapt to the current network

status and future network evolution. For the connection between different shelves inside the

ONU, if any extension shelf is fault, there should be  no infection to other extension shelf.

4.1.9  The ONU shall have the capability to evolve to an Access Media Gateway (AMG) on the

same system platform providing a seamless migration to NGN network in future. The bidder

has to submit adequate document with sketch to proof it.

4.1.10  The ONU must support V5.2 and H.248 uplink concurrently on a single hardware platform,

providing a smooth migration from TDM to IP-based NGN network The TDM voice and

Voice over IP services must be allocated flexibly to specific end users without limitations.

4.1.11  The ONU must support Self-Switching function within it’s subscriber, in case of failure of

link with OLT. In future, after ONU is upgraded to the AMG in the same hardware platform,

the ONU must support Self-Switching function, in case of failure on the H.248 link to the soft

switch, ONU must be able to retain existing RTP connection, and enabling new call to be

established within itself.

4.1.12  Whenever a call is established within the ONU own subscribers, the DSP resources with OLT

shall not be occupied, saving those DSP resources for other outgoing calls connection and

improving voice quality.

4.1.13  The system shall be able to support remote cascading by TDM mode G.SHDSL via twisted

pair, which shall be deployed in area lack of transmission resource of fiber optic.

4.1.14  All the type subscriber related activities (such as ana

4.1.15  The proposed equipment must support DHCP option 60/82 and PPPoE intermediate agent.

4.1.16  OLT/ONU should support port-based leased line access.

4.1.17  The Multi service Access Network Equipment must support –

(a)  IGMP snooping with IGMP messages forwarding to the network

(b)  IGMP proxy

(c)  IGMP static join function for fast zapping must be supported.

Each   Deviation from clause 4.1.1 to 4.1.5 will be treated as “Material” and any deviation from clause

4.1.6 to 4.1.16 will be treated as “Major” Deviation.

4.2 Functional Requirements

4.2.1 Basic Interfaces

4.2.1.1  The OLT Equipment should provide following Interfaces

a.  Digital trunk Card supporting V 5.2 protocol to connect with the Local

Exchanges.

b.  STM-4 & STM-1 optical  interface for transmission

c.  FE and GE interface to connect with data equipment. The interface protocol

provided should conform to the relevant regulations of IEEE802.3z.

d.  Clear Channel E1 to connect with Digital  Data Network or MUX

Deviation will be treated as “Material”.

4.2.1.2  The Indoor ONU Equipment should support following interfaces-

a.  POTS  line card to provide basic telephony service

b.  ADSL Line card to provide simultaneously voice and internet service

c.  Fast Ethernet Interface Optical card to provide internet service over optical fiber at

a distance of about 10 km. The interface protocol provided should conform to the

relevant regulations of IEEE802.3z.

d.  VDSL subscriber line card

e.  G.SHDSL interface card

f.  nX 64 kbps interfaces

Deviation will be treated as “Material”.

4.2.2 Transmission Interfaces

4.2.2.1 The OLT Equipment should provide STM-1 or STM-4 Interface and the interface should

support at least 10 km distance to connect with it’s ONUs

4.2.2.2  The ONU Equipment should provide STM-1 or STM-4 Interface and the interface should

support at least 10 km distance to connect with it’s OLT.

Deviation will be treated as “Material”.

4.3.   Subscriber Interfaces

4.3.1  The G.SHDSL interface must conform

a.  the specifications of G.SHDSL/ADSL2+ ANNEX M

b.  should support  all integral multiples of 64kb/s from 64Kb/s to 2.3Mb/s in both

directions

Each of the deviation will be treated as “major”.

4.3.2  ADSL interface should be provided and conform to

a.   the specifications of ITU-T G.992.1   (including Annex B) and G.992.2.

b.  It should be able to interconnect with third party CPE.

c.  should support ADSL2+ to comply with G.992.5.

d.  should support automatic selection of ADSL, ADSL2, ADSL2+.

e.   ADSL access equipment should have certain LAN access function.

f.  All integral multiples of 32kb/s from 32kb/s to at least 6.144Mb/s in downstream;

g.  all integral multiples of 32kb/s from 32kb/s to at least 640kb/s in upstream should be

supported.

Each of the deviation will be treated as “major”.

4.3.3  Ethernet interface ONU should support

a.  The interface protocol provided should conform to the relevant regulations of IEEE802.3z.

b.  FE and GE interface must support transparent transport and L2 switch function both in the

same board.

c.  FE and GE board, the convergence direction must not be less than 24.

d.  “The Ethernet (FE and or GE) interface, to connect individual subscriber, should be of optical interfece. Electrical Interface can be used only to connect network equipment of same premises.

e.  FE and GE board must support QinQ and MPLS label

f.  FE and GE can support LPT (link path through) function.

g.  FE and GE should support Jumbo frame packet.

h.  Should support bandwidth control (Rate limit) with a granularity of  at least 64Kbps.

i.  The Trans-receiver interface should support at least 10 km distance

bidder can provide additional modular switches with required capability to provide support

mentioned in h & i .

Each of the deviation from a to g will be treated as “major” and deviation from h & i  will be

treated as “Material”

4.3.4  The Analog subscriber lines  interface should support

4.3.4.1 Electrical properties

Subscriber loop resistance,

max. 1200 Ohm

Subscriber loop resistance including a telephone set   max. 1800 Ohm

SL insulation resistance:

Wire to wire

min. 20000 Ohm

Wire to ground

min. 20000 Ohm

SL wire to wire capacitance

Wire to ground

not more than 0.5 mkF

Equipment attenuation

max.  1 dB

Support of program management by the enhancement level -3dB – 3dB (Tx)

-7dB – 7dB (Rx)

Near end attenuation on

1020 Hz frequency

not more than 69.5 dB

Dialing unit transmission rate

7-13 pulses/s

Operating voltage

- 42 V – - 72 V,

Nominal voltage

- 48/60 V

Subscriber boards protection              in compliance with ITU-T K.20

4.3.4.2  Protection of subscriber terminals (ports) against over-current and over-voltage should be

provided (MDF)

4.3.4.3  Every port must have power supply management to decrease board over-heating.

4.3.4.4  Protection of subscriber terminals against short circuit, circuit or leaking between A or B and

earth, or short circuit between two ports should be provided on the board.

4.3.4.5  Bidder must provide detailed description of subscriber board protection mechanism.

4.3.4.6  Must support

a.  ordinary and reversal-polarity

b.  2W/4W Analog leased line

c.  12 / 16 KHz Metering

Each of the deviation will be treated as “major”.

4.4. Management Interface

4.4.1   The equipment should provide management interfaces that are used for local maintenance and

management. The bidder should tell the types and the rate of these management interfaces.

4.4.2  The equipment must provide management interfaces that are used for remote centralized

maintenance and management. The bidder should tell the types of these management interfaces.

Each of the deviation will be treated as “major”.

4.5  After      power failure and service recovery the OLT/ ONU should return to the previous

running status before power failure.

Deviation of clause 4.5 will be treated as “material”.

4.6  Power Supply Requirements for ONU

4.6.1   The present equipped capacity of the rectifier will be at least double  to capacity required for

capacity of ONU. The design shall be based on parallel redundant N+1 system.  One rectifier

module shall be reserved for standby purpose in case of any of the active rectifier modules

fails.

4.6.2     The rectifier system shall be modular in design.

4.6.3     The rectifier AC input range is from 160~285VAC

4.6.4  The rectifier shall be of the latest technology and must be of the switch mode type. Temperature

compensation circuit to adjust float voltage against temperature and low voltage disconnect /

reconnect must be provided in the system.

4.6.5  The modular rectifier suite shall consist of control module and distribution module.

4.6.6  Battery temperature compensation function is necessary for monitoring modules

4.6.7  Automatic battery testing facility

The rectifier must have automatic battery discharge facility with the following

requirements:

a)  Facility can be disabled or enabled,

b)  Time, date and duration of the test can be set through the controller,

c)  Once activated, the output voltage of rectifier shall be reduced to below 43.2VDC

(settable) and battery is discharged to the load.

d)  If the voltage drops below a preset voltage (usually 48V and settable) before the test

period, an alarm shall be triggered to indicate battery failure.

e)  If there is a previous power failure and to prevent wrong battery test results, a settable

period shall be programmed in the controller to prevent any battery test. Period shall be

settable up to 1 week.

4.6.8  Rectifier capacity shall be based on recharging requirement.

4.6.9  Standby battery time is 8 hours for present capacity of ONU with recharging time within 10

hours to 80% capacity after fully discharge.

4.6.10  The bidder has to submit the detail calculation of battery & Rectifier power requirement to

justify the proposed capacity.

Any deviation from 4.6.2 to 4.6.10 will be treated as “Major deviation”

4.8  Main Distribution Frame (MDF)

The ONU shall be equipped with MDF for subscriber connection. This may be inbuilt with ONU rack or may be separate. The MDF shall be of modular structure, miniaturized to the extent possible and easily maintainable. The mechanical structure shall be back-to-back for Vertical and Horizontal side. The cable-pair insertion shall preferably be punch-type; the blocks shall allow insertion of jumper-wires of sizes 0.4 mm to 0.6 mm dia. Any deviation shall be treated as “minor”.

ii)  Each of the MDF shall have the following minimum criteria and any deviation shall be treated

as “minor”.

a)  Minimum number of total available pairs = Equipped subscriber capacity.

b)  Number of OSP pairs in each block = 100 (or 10 x 10).

c)  Grounding: Less than 2 ohms.

iii)  Each MDF shall be fully equipped with 5-point protection device assemblies. The protection

shall be of the following type. Absence of such protection in the MDF shall be treated as "major

deviation".

P1 = P2 =  Over-current Protection (Ceramic or Glass or others) shall become open-circuit on

a – wire

P1

P3

Line Side

P5

Exchange Side

P4

b – wire

P2

Over-current.

breaking voltage      : 180V AC

breaking current      : 1.25 A

breaking time    : 2 ms

P3 = P4 =  Over-voltage and Surge Protection (gas discharge or other type)

shall become open-circuit on over-voltage or surge.

Nominal Voltage      : 180 – 380V AC

Nominal Discharge Current    : 1.3 A

Nominal Impulse Discharge Current  : 100 A

Nominal Resistance      : > 100 Mohms

Current Turn-off Time    : < 200 µs

P5 =  The common point; shall be connected to the frame ground.

a)  The entire assembly shall preferably be enclosed in a single unit but the individual protectors may

also be separate units;

b)  If the protector assembly is taken out of the slot, the circuit between the line-side and exchange-side

for both a-wire and b-wire must become open-circuit;

a)   The assembly shall preferably be one for each cable-pair but multiple-pair assemblies will also

be acceptable;

b)  The assembly shall provide facility to detect & measure presence of any AC voltage or current;

c)  The faulty protection-units inside the assembly shall preferably be changeable in the field;

d)  Facility shall be provided so that if any of the assembly becomes faulty (either the over-current

or over-voltage device), it will trigger an alarm-loop. The bidder will also provide visual and audio

alarm units, with that loop, inside each MDF;

e)  The supply shall include 125% units of the cable-pairs available of each MDF.

iv)  Each of the MDF for ONU shall include supply of at least 20% spare for blocks.  Any deviation

shall be treated as Major.

Book Two

Chapter 5

REQUIREMENTS OF THE OPERATION AND MAINTENANCE FACILITIES

The system should include a Network Management System (NMS)  for proper operation and maintenance of all the Multi Service Access Network Equipment covered by this purchase. The NMS shall include all necessary hardware and software to be installed on a complete turn-key basis including design, installation, testing and commissioning at Moghbazar. Bidder can propose one or more suitable hardware platform for the proper functioning of NMS. However, the main hardware system that will perform the operation and maintenance of ONU for POTS,ADSL & G.SHDSL subscriber, should have following characteristics as described 5.1.1 & 5.1.2. The hardware for other NMS should be of SUN Solaries or equivalent or better high quality with useable 100 GB Hard Disk Drives in RAID configuration and based on UNIX or LINUX operating system. Any deviation will be treated as “Critical Deviation.”

5.1   Hardware/System Requirements of NMS

5.1.1 Server System

The NMS shall be equipped with SUN or Solaris  equivalent  or  better high-quality server system in duplicated configuration. The Operating Software shall be based on the latest version of UNIX or LI NUX. The internal network architecture shall be Ethernet LAN. The deviation shall be treated as “Material Deviation”.

5.1.2 Memory Devices

a)  The NMS system shall have Hard Disk Drives in RAID configuration as the primary

memory device. At least 1(one) External Compact Disk Re-writable Drives shall be provided to

act as the secondary memory device.

b)  The capacity of the hard drive shall be at least 100 GB usable SCSI disk space

configured as RAID level 5 with one disk as hot spare.

The deviation shall be treated as “Major Deviation”.

5.1.3  Server and Operator Terminals

a)  Server Terminal has  to be provided at NMS site.  The Server Terminal shall be

complete in all aspects to work as PC and shall be equipped with Monitors (at least

17” wide), Hard Drive (at least 150 GB), RAM (at least 2 GB) and DVD writer .

b)  Operator Terminal(s) shall be there at all OLT sites.  Operator Terminal shall be

equipped with Monitors of at least 17” wide LCD ), Hard Drive (at least 150 GB), RAM

(at least 2 GB), DVD Drive. At least 2(three) nos. of such

terminals shall be provided.

c)  2.5” Portable USB-Mass storage device for taking data back up.

d)  10 (ten) nos of USB Pen drive with necessary capacity of at least 8 GB.

e)   DC power is preferable. If DC option is not available the inverter should be capable of

taking the load along with other equipment (Printer, LCD panel etc.)

The deviation shall be treated as “Major Deviation”.

5.1.4  Printers in the NMS

The supply shall include at least 1(one) number of Printer having following specifications

connected in the LAN of the NMS.

a)  Resolution  :  600 X 1200 pixels Minimum

b)  Pages per minute  :  Minimum 32

c) Memory  :  32 MB

d)  Paper Tray  :  Three trays, one of 100-Sheets and two of 500-sheets

e)  Network Interface Card  :  10/100 base - TX

f)  Paper size  :  A3/A4/ Legal/Letter

The deviation shall be treated as “Major Deviation”.

5.1.5 Inverters

The supply shall include necessary inverters for the equipment that uses AC sources. The

inverters shall be on N+1 redundancy configuration and shall use the exchange -48V DC as

source power. The deviation shall be treated as “Major Deviation”.

5.2   Software Requirements of NMS

5.2.1 Password Protection

The main features and data of the software shall be protected by multi-level password control.

Modification of the Network data and Subscriber configuration data shall also be protected by

passwords. The system password will not be erased or corrupted during system re-boot and/ or

redundant server switchover or for any other reasons. Deviation shall be considered as

“material”.

5.2.2   Immunity against propagated faults

All modules of the Software shall be immune against propagation of faults from any other

software or hardware modules and shall be protected against any mutilation of data. The faulty

software module shall also not propagate its own fault to any other software or any hardware

modules. Deviation shall be considered as “material”.

5.2.3  The language of the instructions shall be in English.

5.2.4  For commands which will change basic network/system data or which may cause

reconfiguration of the system or critical errors, provisions will be provided for verification

before execution

5.2.5  Records of all executed commands shall be kept in log files and these files shall be stored in

system hard disk

5.2.6  Any deviation (each of them) from the characteristics mentioned in 5.2.3 to  5.2.5 shall be

considered as “major”.

5.2.7  The bidder shall note that if its language of instruction is in any language other than English, its

system shall be considered to be having "Change of Substance".

5.3     Guarantee for Introduction of new Features

5.3.1  The bidder shall guarantee that, if  BTCL or TSS requests for introduction of any new/ additional

subscriber and/or system features in the supplied system, the bidder shall try its best to do so.

5.3.2  The price for such new/ additional features shall be logical and realistic and shall be fixed up

by mutual discussion.

Any deviation shall be considered as “major”.

5.4  Guarantee for up-gradation of Software Version

5.4.1The Bidder shall guarantee that it will inform  BTCL as well as TSS for all subsequent up-grades of the software

version of the supplied system.

5.4.2 If the upgrade becomes mandatory for any expansion of the supplied system or addition/

modification of any prevalent subscriber feature, such software upgrades shall be done "free of

charge" to TSS.

5.4.3 If such upgrade becomes mandatory for proper operation & maintenance of the network in its

present configuration and form, such upgrades, including supply of new software and

hardware, shall be done "free of charge" to TSS.

5.4.4  If any non-mandatory upgrade is done on request from BTCL or TSS, but does not involve any change

or addition in hardware, the bidder, upon request from BTCL or TSS, shall install such upgraded

software "free of charge" to TSS.

5.4.5  But, if any non-mandatory software upgrade, to be done at the request of BTCL or TSS, involves any

hardware change and/ or additional hardware, charges will be incurred for prices for the

changed and/ or additional hardware and the new software. In such cases, the prices for such

new and/ or additional hardware and software shall be fixed on mutual agreement and in

consistent with the market prices prevalent at the time of such request.

5.4.6 Bidder’s refusal to agree to the above sub-clauses 5.4.1 to 5.4.5. shall be considered as “material

deviation”.

5.5  Guarantee for Software

The Bidder shall guarantee that, the Software of the system will run without any technical

hazard for at least up to 5(five) years after the date of effect of FAC. If any fault and/ or bug is

detected within this period, the bidder shall correct these faults and debug the software at his

own costs and at “free of charge” to TSS. Bidder’s refusal to agree to this guarantee shall be

considered as “material deviation”.

5.6  Functional Requirements of NMS

5.6.1  The NMS shall have the capability to support the following management functions for all

elements:

a)   Fault Management

b) Configuration Management

c) Performance Management

d) Security Management

e)  Capacity and Planning Engineering Tool

All the management functionalities shall be implemented in the NMS as a set of interactive

application components using client-server architecture and can be vertically and horizontally

integrated.

5.6.2  The NMS should support the following:

a)   Graphical User Interface (GUI)

b)   Real-time alarm display and collection

c)   Card/circuit level diagnosis

d)   Interface line status monitoring, both subscriber lines and network interface.

e)   Performance monitoring and traffic measurement.

f)   Network/NE configuration management.

g)   Routing table management

h)   SNMP-based network management interface(s) to support third party network

management system.

i)   adaptive to ITU-T Q3/CMIP.

j)   Latest version of the Windows NT, Solaris OS and HPOV or any management system

available.

k)  Implementation of software patches and releases on the NGN nodes remotely.

5.6.3  Basic Features and Capabilities

The NMS shall provide:

a)  Preferably a single Application Program Interface (API) for all network elements regardless

of Brand and Model.

b) Configuration planner for simplifying the task of future network planning and

configuration.

c) Automatic copy of configurations at device, cards, and ports level to the customer

information database system within the NMS.

d)  Network Integrity check at the network, device, card, and port levels.

e)  End to end path management.

f)  Advance alarm management setting for priorities and types.

g)   Multiple network managers support with different access authorities.

h)  Network element status displayed by colors.

i)  Identification of problems through event correlation. It should intelligently correlate events

into high level alarms, immediately pinpointing the root cause of network problems.

j) Web-based user interface.

k) Scalable architecture

5.6.4  Fault/Alarm Management

The NMS shall support (but not limited to) the following fault and alarm management

capabilities:

a)   Detected errors/unusual  network behavior should be isolated and controlled.

b)   Results of errors/unusual network behavior should be displayed in graphical and tabular

form.

c)   Alarm facilities should permit the easy identification and correction of faulty element.

d)   Alarms should have a status of active, deferred, or cleared and should be in active state

when first received.

e)   The severity of the alarm, full alarm message and time of delivery should be available

for display and are logged in the alarm database.

f)   The administrator should be able to set various thresholds for alarm reporting, including

filtering by severity, number of occurrences within a given period and interval between

occurrences.

g)  Management System should provide alarm signals confirmation, including user ID

confirmation and time of confirmation

h)  All test result should be saved in data base

5.6.5  Configuration Management

The Configuration Management should initialize and close down manage objects, collect

information on demand about the current condition of the network, obtain announcements of

significant changes in the condition of the network, and change the configuration of the

Network and the Network Elements.

5.6.6  Performance Management

The NMS should support, but should not be limited to the following performance management

capabilities:

a)   Monitor network throughput and real-time Bit Error Rate must be supported.

b)   Set thresholds for various variables, such as error rates or link utilization.

c)   Continuous background diagnostics during system uptime are required for early

detection of fault conditions and timely activation of alarms.

d)   Log and save all or defined events for present and future reference.

e)   All man-machine interfaces shall be in a Graphical User Interface.

Any deviation of the above requirement shall be treated as “Major Deviation”.

5.6.7  Security Management

The NMS should support (but not limited to) the following security management capabilities:

a)   Secure access between network elements and the network manager.

b)   The system should incorporate security measures against unauthorized personnel to

access the office data/programs and entering of commands.

c)   Several access levels according to the order of their influence on program

performance should be identified with the corresponding password.

Any deviation of the above requirement shall be treated as “Major Deviation”.

Subscriber Circuit Testing and Phone Testing Requirements

I. Subscriber Circuit Testing

1) Pulse dialing

Break-make ratio 1: (1±0.2)

Pulse speed: 12.5±1pps

Number interval: =400ms

2) Dual tone dialing

Frequency deviation: ±1.5%

Level: Low frequency group: -9±5dBm

High frequency group: -7±5dBm

Dual frequency signal level difference: 2±1dBm

Total distortion: 20dB lower than fundamental wave level

Signal limit duration: > 40ms/bit

Signal interval duration: > 40ms

II. Phone Testing

1) Ringing current

Voltage: 75V±15V

Frequency: 25Hz±3Hz

Break-make ratio: 4s: 1s

Time deviation: ±5%

2) Signal tone (450Hz)

Frequency: 450 Hz±25Hz

Level: -10±3dBm

Harmonic wave: <10%

Busy tone: break-make duration 350ms: 350ms, time deviation <±10%

Ring back tone: break-make duration 1s: 4s, time deviation <±10%

3) Pulse dialing test

Dialing speed: 8~20pps

Break-make ratio: test range: (1.0~3.0)

Test error: ±5%

4) Dual tone dialing performance test

Frequency and frequency deviation

Frequency (standard: low frequency group 697, 770, 852, 941Hz, high

frequency group 1209, 1336, 1477, 1633Hz)

Frequency deviation: reliable receiving is ±2%; surely no receiving is ±3%; and

not surely receiving is ±2%~±3%

Level:

Signal frequency receiving range in dual frequency mode: -4~-23dBm

Signal frequency non-operation level in dual frequency mode: =-31dBm

Dual frequency level difference: =6dBm

Signal limit duration: 80ms/bit

Signal interval duration: 40ms

5) Opposite polarity

Time interval: 5s

Time deviation: ±5%

6) Howler tone

Frequency: 950Hz±50Hz

Frequency: 6dBm~140dBm

Harmonic wave: <10%

7) Loop resistance measurement

Test range: 0~3k

Test error: ±5%

8) Test speed

Test duration of twelve indices for the subscriber line: <30 seconds

Any deviation of the above requirement shall be treated as “Major Deviation”.

.

SPECIFIED

CHARACTERISTICS TEST

RESULTS

METHODS

.. ±. µm

Mode field diameter

.. ±. µm

Cladding diameter

Coating diameter  TRANSMITTED  .. ±. µm

Mode field concentricity error  NEAR-FIELD  <.. µm

Cladding non circularity  TECHNIQUE  <. %

<.. µm

Cladding concentricity error

Continuous tensile test                SCREEN TEST                     0.5 daN

... <lc<... nm

Cut-off wavelength lc              TRANSMITTED POWER

TECHNIQUE

<.. dB/km

Unit attenuation

CUT-BACK

TECHNIQUE

<... dB/km

for 1285 <l < 1330 nm

for l = 1550 nm

BACK SCATTERING

0.1 dB

Transmission curve regularity

TECHNIQUE

AT 1300/1550 NM

Chromatic dispersion

<.. ps/nm.km

<.. ps/nm.km

<.. ps/nm.km

coefficient

for 1285 <l < 1330 nm

for 1270 < l < 1340 nm

for l = 1550 nm

TIME-DOMAIN or

FREQUENCY DOMAIN

MEASUREMENT

ps/(km)

Polarisation Mode Dispersion

Book Two

Chapter 7

REQUIREMENTS OF THE ANCILLARY FACILITIES

7.1   Patch Panel at different sites

(i)  BTCL is installing IP DSLAM equipment under another Tender. To install MDF patch

panel, to lay internal cable from MDF room to DSLAM room are the scope under this

project. The following sites shall be equipped with required number of Patch panel in

the existing Main Distribution Frame (MDF) room of BTCL. There shall be two patch

panels. One patch panel shall be used for termination of subscriber cables coming from

telephone exchange via horizontal side blocks and the other shall be used for

termination of subscriber outside plant copper cable network via vertical side blocks (as

described in the figure below).

(ii)   The cable-pair insertion shall preferably be punch-type; the blocks shall allow insertion

of jumper-wires of sizes 0.4 mm to 0.6 mm dia. The patch panel may be installed in

existing MDF, if there is facility. Otherwise the bidder shall provide MDF frame.

However, the bidder shall quote MDF rack/frame and patch panel (tag block) separately

for all the sites (except secretariat). The actual quantity will be finalized during BoQ

preparation upon required survey. Any deviation will be treated as “Major”

(iii)    Patch panels at each MDF shall have the following minimum criteria and any

deviation shall be treated as “minor”.

a)  Minimum number of total available pairs in Exchange side patch panel as shown

in the below list

b)  Minimum number of total available pairs in Subscriber side patch panel : as shown

in the below list

Subscriber side patch

panel                   Exchange side patch panel

Requirement                      Requirement

3500

3500

1 Moghbazar, Dhaka

4000

4000

2 SBN, Dhaka

5000

5000

3 Gulshan, Dhaka

4000

4000

4 Central, Dhaka

1500

1500

5 Chawkbazar, Dhaka

1500

1500

6 Comilla

1500

1500

7 Sayedabad, Dhaka

1500

1500

8 Fakirapool, Dhaka

2000

2000

9 Mirpur, Dhaka

3000

3000

10 Nilkhet, Dhaka

4000

4000

11 Uttrara, Dhaka

1500

1500

12 Narayangonj, Dhaka

1500

1500

13 Khilgaon, Dhaka

1500

1500

14 Cantonment, Dhaka

3000

3000

15 Agrabad, Chittagong

1000

16 Nandan Kanon, Chittagong                         1000

1000

1000

17 Central Sylhet,

1000

1000

18 Central, Khulna

1000

1000

19 Bogra

1000

1000

20 Barisal

1000

1000

21 Rajshahi

1000

1000

22 Gazipur

1000

1000

23 Savar

1000

1000

24 Mymensingh

1000

1000

25 Jessore

Total

49000

49000

c)  Maximum number of termination pairs in each block of patch panel : bidder’s choice

d)  Grounding: Less than 2 ohms

7.2  Optical Distribution Frame (ODF)

The Bidder shall provide necessary Optical fiber termination facility (Optical Distribution

Frame) for terminating optical fibers to connect LAN  ports of the switch.

i)  Each of the ODF shall have the following criteria and any deviation shall be treated as

“minor”.

1)   Adopting the popular 19” rack

2)   having splicing and distribution module

3)  Stable equipments for fixing, stripping and grounding of the optical fibers

4)   Suitable for ribbon and non-ribbon optical fibers

5)   Suitable for installation of FC, SC and ST adaptors

6)  Optical fibers, fiber optic pigtails and jumpers are separate, without disturbing each

other

7)  Fiber optic cable management

ii)  Each of the ODF shall be properly grounded as per standard specification.

iii) The ODF shall preferably be located in the same room where Switch is installed , but it can

also be shifted to any other suitable room on mutual agreement. The maximum distance

between the switch position and the ODF shall be kept to 30 meters.

iv)  The supply, per site, shall include ODF termination facility as per annexure.

v)  The ODF capacity shall as below-

Site

Requirement

Moghbazar, Dhaka  24

24

SBN, Dhaka

48

Gulshan, Dhaka

48

Central, Dhaka

Chawkbazar, Dhaka                       24

24

Comilla

Sayedabad, Dhaka                       24

Fakirapool, Dhaka                       48

Secretariat, Dhaka                       48

24

Mirpur, Dhaka

48

Nilkhet, Dhaka

48

Uttrara, Dhaka

Narayangonj, Dhaka                      24

Khilgaon, Dhaka                       24

Cantonment, Dhaka                        24

Agrabad, Chittagong                        24

Nandan Kanon, Chittagong            24

24

Central Sylhet,

24

Central, Khulna

24

Bogra

24

Barisal

24

Rajshahi

24

Gazipur

24

Savar

24

Mymensingh

24

Jessore

7.3 Tip Cable

The bidder shall supply additional tip cable to TSS for jumpering purpose in the MDF in

order to provide ADSL service to the telephone Subscribers . The tip cable shall be of 0.4 mm

dia. The supply shall include 200 Kilometer-pair tip cable.

7.4  Internal Cable from MDF patch panel to IP DSLAM room

Bidder has to install 0.4 mm internal cable from MDF patch panel to IP DSLAM room to

connect with splitter .

Book Two

Chapter 8

CRITERIA FOR EVALUATION OF BIDS : EVALUATION OF SUBSTANTIAL RESPONSIVENESS

8.1 The criteria for evaluation of substantial responsiveness of the received bids of this

tender shall be according to the clauses described in this chapter of the tender document. If

any bidder refuses to agree to all clauses of this chapter, his bid shall automatically be

considered as “Substantially Non-Responsive”.

8.2  However, relevant clause(s) stated elsewhere in this document shall also be applicable if such

clause(s) do(es) not contradict any or many clause(s) of this chapter.

8.3  Moreover, relevant regulations of the The Public Procurement Regulations 2006 (PPR

2006) published by The Government of Bangladesh (and available in web site

www.cptu.gov.bd) shall also be applicable. It may be noted that, if any clause or sub-clause

of this document is detected to be in contradiction to any regulation or part of any regulation

of the said PPR 2006, the text and definitions of the relevant regulation or its part of PPR

2006 shall prevail. The decision in this regard shall be finalized by TSS.

8.4  The process of evaluation shall be in the following order:

i.  Determination of Eligibility of the bidders

ii.  Evaluation of Responsiveness of the eligible bidders.

iii.  Financial Evaluation of Responsive bids and arranging the bids in ascending order on

the basis of Evaluated Cost.

iv.  Post qualification for selection of successful bidder

8.5  The TEC will first examine the contents of all “Mandatory Documents” of each Bid.

8.6  Bidder who will not give any or many of the required documents as mentioned in

“Mandatory Documents”,  the TEC of TSS shall consider that bid to be “not eligible”

and reject the concerned bid.

8.7  The bids of only those Bidders, whose bids have not been treated as "not eligible" by the

TEC of TSS shall automatically be considered as “Eligible” and shall be considered for

further evaluation.

8.8  Any bid, declared by TEC of TSS to be “not eligible, can not be declared “Eligible” later

on.

8.9  The TEC shall then preliminary examine the Tender documents of the Eligible Bidder to

confirm that all documents in the “Mandatory Document” folder have been submitted in the

prescribed format and determine the completeness of each document. If content of any of the

Mandatory Document(s) do not fulfil the requirement of the respective tender clauses the bid

shall be treated as “Non-Responsive”.

8.10  The TEC shall also assess the offered equipment’s qualifications and bidder’s qualifications

submitted in “Detail Technical Documents” folder. If TEC find that the requirement is not

fulfilled as per Tender document the bid will be treated as “Non-Responsive”.

8.11  If, for any Bidder, the “Financial Documents” does not contain any of the Documents listed

in Clause – 1.8 of Chapter 1 of this Book, the TEC of TSS shall treat the bid to be "Non-

Responsive" and shall not continue with further evaluation of the bid.

8.12   Any bid found to be “Non-Responsive” during preliminary examination shall not continue

with further evaluation of the bid.

8.13  After preliminary examination, the bids will be examined on technical aspects. During

evaluation, TEC shall consider bidders’ compliances to various clauses and sub-clauses of

this tender; but shall have the authority to conclude its own decision about such compliances.

8.14  If the bidder does not give any statement to its compliance to any of the tender clauses or sub-

clauses or drops any clause or sub-clause in the “Schedule of Compliance”, its' compliance

to that clause/ sub-clause (as applicable) shall be treated as “not complied” to that particular

clause/ sub-clause.

8.15  If the bidder puts any condition to his compliance to any of the tender clauses and/ or sub-

clauses, its' compliance shall be treated as “not complied” to that particular clause and/ or

sub-clause.

8.16  TEC shall also consider the contents of various attached documents. If any content of the

attached documents contradicts the compliance statement of the bidder to any of the clauses

and/ or sub-clauses, the bidder shall be treated as “not complied” to that particular clause and/

or sub-clause. In all of such cases, decision of TSS shall be final.

8.17  If any component equipment of the offered system is already working in BTCL network, for

conclusion about compliance to any clause/sub-clause, BTCL's practical field experience

shall be given priority over bidder's statement regarding the relevant capabilities,

performance, working reliability in field, operation & maintenance aspects, user’s satisfaction

etc. of all those equipment. BTCL&TSS shall have the authority to draw its own conclusion

regarding this aspect.

8.18  If, in answer to any query by TEC the bidder provides any or many clarifications to its bid,

TEC shall consider those clarifications. However, if such clarifications contradict the relevant

statements given in his original offer, the offered clarification(s) shall be disregarded.

8.19  The following deviations of any offer will be treated as “minor deviation” of the bid :

8.19.1  Any deviation which has already been termed as “minor deviation” in this tender document.

8.19.2  If specification of the offered equipment contain any "non conformity" from the tender

specification.

8.19.3  If the bid BoQ has any shortage of quantity in any of the required item, where clause 8.21.4 or

8.24.3 is not applicable (for each of such short-quoted item).

8.20  Any item of “minor deviation” shall earn a score of 1(one) “penalty point”.

8.21  The following deviations of any offer will be treated as “major deviation” of the bid :

8.21.1   Any deviation which has already been termed as “major deviation” in this tender document.

8.21.2  If the offered bid is "non compliant" to any clause or sub-clause of this document (for each

of such non compliant clause or sub-clause).

8.21.3  If specification of the offered equipment contain any "major deviation" from the tender

specification.

8.21.4  If there is any shortage in the list of quoted hardware and if such shortage can be

accommodated in functional and physical structure of the bidder’s offered equipment (for

each of such shortages).

8.21.5  If the bidder fails to quote for any optional item of the tender (for each of such failure).

8.21.6  Any clarification given by the bidder which contradicts statements given in his original offer.

8.22  Any item of “major deviation” shall earn a score of 5(five) “penalty points”.

8.23  The following deviations of any offer will be treated as “material deviation” of the bid :

8.23.1  Any deviation which has already been termed as “material deviation” in this tender

document.

8.23.2  If combination of two or more deviations (either minor or major) in bidder's offered technical

specification or conditions amounts to any contradiction of the functional structure of the

system as specified in the tender.

8.23.3  If there is any shortage in the quantity of any hardware item or in the list of system hardware

and if such shortages can not be accommodated in functional and physical structure of the

bidder’s offered equipment.

8.23.4  If the Bidder has changed either the language or format of any of the different forms attached

with this document.

8.23.5  Any clarification given by the Bidder which changes the nature or structure of his original

bid.

8.24  Any item of “material deviation” shall earn a score of 50 (fifty) “penalty points”.

8.24  The following deviations of any offer will be treated as “change of substance” of the bid:

8.24.1  Any deviation which has already been termed as “change of substance” in this tender

document.

8.24.2  Any contradiction in contents of different sections of attached documents which amount to

change of nature or structure of the bid itself.

8.24.3  If the bidder refuses to provide answers or does not provide answers within stipulated time to

any requested clarification(s).

8.24.4  Any condition, set forth by the bidder, in the Financial Documents.

9.24.5  If the Bidder changes the language or format of any of the bid proforma.

8.24.6  If combination of two or more deviations (minor and/ or major and/ or material) in technical

specification or conditions in the offered bid combined amounts to such a deviation that the

offered system does not at all satisfy the overall functional requirement and/ or objective of

this procurement proceeding.

8.24.7  If any Certificate or any other document attached as part of the bid is found to be false or

unauthentic.

8.24.8  If, for any Bidder, the “Financial Documents” part does not contain any of the prescribed

BoQ Forms, duly filled up.

8.24.9   If the Bidder wishes to give any discount, it shall be given after the “Total Price” of the bid

either as a lump sum or as a percentage. Any irregular discount shall be treated as “change of

substance”.

8.25  The bid offer, found to be containing any item of “change of substance” shall be treated as

“Non Responsive”.

8.26  All of the evaluated bids will be categorized by adding up the “penalty points” earned by

each offer. The offer of any Bidder which has earned more than 80 (Eighty) “penalty points”

shall be treated as “Substantially Non-Responsive” and the offer which has earned less than

or equal to 80 (Eighty) “penalty points” shall be treated as “Responsive”.

8.27  TSS’s decision to treat any bid as “substantially non responsive” shall be final.

8.28  The bid(s) treated as “substantially non responsive” shall not be considered in the further

stages of evaluation.

Book Two

Chapter 9

CRITERIA FOR EVALUATION OF BIDS :

Evaluation of Financial Parts of Responsive Bids and Selection of Successful Bidder

9.1  The TEC shall evaluate Financial Part of each Tender that has been determined, up to this

stage of the evaluation, to be substantially responsive.

9.2  The total price quoted by the “Responsive” bidder in his bid i.e., “The Quoted Total Price”

shall not be the criteria for selection of the “Successful Bidder”.

9.3  All of the “Responsive” bids will be further evaluated considering all the tender requirements

to calculate the “Evaluated Total Price” of the bid.

9.4  The process of calculation of the “Evaluated Total Price” shall be in accordance with the

clauses described in this chapter.

9.5  TEC shall evaluate the contents of all of the BoQ forms submitted with the bid.

9.6  During such evaluation, the unit prices and discount (if any) quoted by the bidder shall be

considered as final. Change of prices during evaluation stages shall not be allowed.

9.7  There shall be full conformity between the summary or total prices and their related breakups

of unit prices. If any discrepancy is found, the relevant unit prices shall be considered as a

reference price for evaluation purpose.

9.8  The bidder shall quote for all items it deems necessary for turn-key completion of all scopes

of works described in this tender. No subsequent addition of any new item(s) in the BoQ will

be allowed with additional price.

9.9  The successful bidder shall be responsible for turn-key implementation of the project and for

any shortfall of items subsequently detected, it shall be considered that the bidder proposes to

supply those items of required quantities “free of charge” to TSS for this purchase and for

any subsequent purchases.

9.10  If the Bidder has quoted the price for any item as “free” or “zero”, it shall be understood that

the price would be same (i.e. free or zero) for any subsequent expansion up to the minimum

final capacity of the system.

9.11  If, during evaluation, it is found that the bidder has not quoted any or many mandatory

item(s), it shall be considered that the Bidder proposes to supply the non-quoted items of

required quantities “free of charge” to TSS.

9.12  If, during evaluation, it is found that the bidder has quoted for less quantity of any mandatory

item, it shall be considered that the Bidder proposes to supply the shortfall quantity “free of

charge” to TSS.

9.13  In case any Bidder has quoted an under-sized item, it shall be understood that the bidder

proposes to supply any amount of that item to TSS, but of proper size (as described in tender

specification) with the same price i.e. his quoted price for the under-sized item and that this

price would also be valid for any subsequent expansion of the system, any time on demand and

for the entire life-time of the project, i.e., 5(five) years from the date of issuance of FAC.

9.14  In case any mandatory item has been quoted as optional, its price shall be added as mandatory

and the unit price shall be taken from the bidder’s own quotation.

9.15  If the bidder has given any regular discount in the bid, such discount shall be treated in

percentage of the total bid price and each of the unit prices of the bid shall be re-fixed by

reduction with the same percentage [i.e., new unit price = (discounted total price ÷ total price

before discount) x quoted unit price]. Such re-fixed unit prices shall be regarded as the final

unit prices for that relevant item of the bid. Such re-fixed unit prices shall be valid for any

subsequent purchases up to the entire life-time of the project, i.e., 5(five) years from the date of

issuance of FAC.

9.16  For each of the “responsive” bids, TEC shall calculate the “Evaluated Total Price” after making

the relevant and necessary corrections as stated in this chapter.

9.17  All the “Responsive” bids will be listed in chronology of the “Evaluated Total Price”; the bid

with the lowest value of the “Evaluated Total Price” shall be on top of the list; the bidder with

the next higher value of the “Evaluated Total Price”  shall be next to the top; and so on.

9.18  Prior to finalising the Tender Evaluation Report including recommending contract award,  the

Tender Evaluation Committee shall determine whether the tenderer whose tender has been

determined to offer the lowest evaluated total cost has the capability and resources to

effectively carry out the contract as offered in the tender. This shall be termed as “Post

Qualification”.

9.19  Determination of successful bidder shall be based upon examination of the documentary

evidence(s) of the Equipment’s qualification and Tenderer’s qualifications alongwith other

documents submitted by the Tenderer. References or statement submitted by the Tenderers

about his previous or current working experience in BTCL or elsewhere may be verified, to obtain the most up-to-date information available concerning the Tenderer.

9.20  As part of the post-qualification task, the TEC shall take necessary steps, whichever fits

desirable and practical to them, to verify information contained in its tender.  The TEC shall

also verify the contents of all the documentary evidences. The committee shall have the

authority to contact the persons/ organizations issuing the documents to ascertain the

authenticity. If for any bidder, either the content or the source of any of the supplied document

is found to be unauthentic, or if the issuing organization/ person refuses to certify the

authenticity of any document, the Tender Evaluation Committee of TSS shall treat the bid to

be "Non-Responsive" and shall not continue with further evaluation of the bid. If any

document is proved to be fake or unauthentic or any information is found to be incorrect,

TSS shall take appropriate measures as per The Public Procurement Regulation 2006.

9.21  An affirmative determination shall be a prerequisite for award of the Contract to the Tenderer.

A negative determination shall result in rejection of the Tenderer’s Tender, in which event

TSS shall proceed to the next lowest evaluated Tender to make a similar determination of

that Tenderer’s capabilities to perform satisfactorily. In this process the “Successful Bidder”

will be selected.

9.22  TSS  reserves the right to accept any Tender, to annul the Tender process, or to reject any or

all Tenders, at any time prior to contract award, without thereby incurring any liability to the

affected Tenderers, or any obligation to inform Tenderers of the grounds for TSS’s actions.

9.23  After the opening of Tenders, information relating to the examination, clarification, and

evaluation of Tenders and recommendations for award shall not be disclosed to Tenderers or

other persons not officially concerned with the evaluation process until after the award of the

Contract is announced.

9.24  If any guideline not covered by this chapter but required during evaluation process, the TEC

shall consult with PPR 2006.

Book Two

Chapter 10

MECHANISM FOR AWARDING THE CONTRACT

10.1  Not withstanding whatever is stated in other clauses of the tender documents, the mechanism

for awarding the “Purchase Contract” of this tender shall be according to clauses described in

this chapter of the tender document.

10.2  A letter of intent, accompanied by a draft contract, will be issued by TSS to the “successful

bidder”.

10.3  The successful bidder will be required to give its answer, within 15(fifteen) working days after

issuance of that letter of intent, stating its willingness to sign the proposed contract.

10.4  If no answer is received by TSS within this stipulated time, it shall be inferred that the bidder

is unwilling to continue with the process of signing of the contract.

10.5  If no answer or a negative answer has been received from the selected bidder, TSS will

unilaterally cancel the letter of intent and start subsequent proceedings of its choice. In such

case, TSS reserves the right to forfeit the bid money of the defaulting bidder.

10.6  Performance Security Bond

10.6.1 The successful bidder shall, with its answer to the letter of intent, have to submit, a

“Performance Security Bond”, as mentioned in the concerned document, in the form of Pay

Order/ Bank Draft/ Bank Guarantee from any recognized Bank in Bangladesh, in favour of

“Managing Director, Telephone Shilpa Sangstha Limited”. The validity of such bond must cover the period up to the commercial launching of services of the first system/node of all systems covered by this purchase or issuance of the first PAC of the system, whichever is later.

10.6.2 The performance security bond will be refundable after issuance of the first Provisional

Acceptance Test Certificate (PAC) of all the systems covered by the contract or after the

commercial launching of services of the first system/node of all systems covered by this

purchase, whichever is later.

10.6.3  If the successful bidder does not submit the performance bond, it shall be deemed that, the

bidder has given a negative answer to TSS 's request for signing of the contract.

10.6.4  Should the bidder fail to launch the commercial services of the first system/node, in time and

way as described in the contract, TSS will be entitled to recover Tk. 1(one) million for each

month or its part of such delay. In case, the total recoverable amount exceeds the amount of the

performance security bond, TSS will reserve the right to terminate the contract and forfeit the

total amount of the performance bond.

10.7  The bidder, after submission of the Performance Security Bond, shall be invited by TSS to

start negotiation on different aspects of the contract and relevant BoQs.

10.8  The bidder shall start negotiation within 15(fifteen) days after issuance of such invitation.

Efforts will be made by both the parties to complete negotiation within the shortest possible

time.

10.9  If the bidder fails to start the negotiation within the stipulated time, it shall be concluded by

TSS that, the bidder is not willing to sign the contract. In such a state, TSS will unilaterally

cancel the letter of intent and start subsequent proceedings of its choice. In such case, TSS

reserves the right to forfeit the bid money of the defaulting bidder.

10.10  The bidder will note that, if it has disagreed to or had proposed any alternate conditions to any

or many clauses or sub-clauses of the proposed draft contract, such disagreement and/ or

alternate proposals shall not be binding upon TSS until and unless amendment(s) to relevant

clause(s) are agreed by TSS before signing of the contract.

10.11  After completion of the negotiation process, representatives of both the parties shall initial

copies of the agreed contract.

10.12  TSS shall take steps for approval of the contract by relevant authorities.

10.13  After approval of the contract by TSS 's relevant authority, representatives of the bidder and

TSS shall sign the final copies of the contract. At least 3(three) copies of the contract shall be

signed in original; one of the copy shall be taken by the bidder and the other two shall be

preserved by TSS.

|  | Required Capacity |  | Bidder's offer |
| --- | --- | --- | --- |
|  | GE interface | V5.2 interface | E1 for DDN | STM-4 | GE interface | V5.2 interface | E1 for DDN | STM-4 |
| Gulshan |  |  |  |  |  |  |  |  |
| Dhaka Cantt |  |  |  |  |  |  |  |  |
| Uttara |  |  |  |  |  |  |  |  |
| Nilkhet |  |  |  |  |  |  |  |  |
| Motijheel |  |  |  |  |  |  |  |  |
| Mirpur |  |  |  |  |  |  |  |  |
| Chakbazar |  |  |  |  |  |  |  |  |
| Saidebad |  |  |  |  |  |  |  |  |
| Rampura |  |  |  |  |  |  |  |  |

Annex 1.1

OLT Design Consideration :

CAPACITY REQUIREMENT OF OLT

2.  0.10 erl for all POTS & ADSL lines

3.  1 E1 per G.SHDSL subscriber

4.  1 Mbps per ADSL subscriber

5.  5 Mbps per FE port

interface required for all  3-8 ONU under that OLT

1.  The required capacity of  different interface has to be determined on the basis of  total

Annex 1.2

Type of ONU with capacity

|  | Type | No of ONU | POTS with ADSL2+ | FE | G.SHDSL | ISDN | STM |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Type A | 15 | 1000 | 12 | 4 |  | STM-1 |
|  | Type B | 17 | 1500 | 12 | 4 |  | STM-4 |
|  | Type C | 04 | 2000 | 12 | 4 |  | STM-4 |

Total    36

1. Number of STM-4/STM-1 Interface requirement for each ONU has to be determined on the basis of following

consideration

- 1 E1 per G.SHDSL subscriber

- 0.10 erlong for all POTS & ADSL lines

- 1 Mbps per ADSL subscriber

- 2 Mpbs per FE port

2. POTS with ADSL means both ADSL and Telephone facilities should be available each subscriber.

|  |  | Annex 1.2(a) |  |
| --- | --- | --- | --- |
|  |  | Area and capacity of ONU |  |
| SI No | Exchange Name | Area of ONU | Type of ONU |
| 1 | Gulshan | 1.Notunbazar Fire service,DESCO office,Badda Thana |  |
|  |  | 2.Bashundhara Residential Area (A Block) |  |
|  |  | 3.Baridhara U N Road (Beside No House 15) |  |
|  |  | 4.Jamuna Future Park |  |
|  |  | 5.Aftab Nagar |  |
|  |  | 6.Middle Badda |  |
|  |  | 7. Tejgaon Indistrial Area |  |
| 2 | Dhaka Cantt | 1.New DOHS Mohakhali |  |
|  |  | 2.Kafrul and Ibrahimpur |  |
|  |  | 3.Manikdi |  |
| 3 | Uttara | 1.Ashkona Hazi Camp |  |
|  |  | 2.Khilkhet |  |
|  |  | 3.Sector-5 |  |
|  |  | 4.Sector-7(Lake Drive Road) |  |
|  |  | 5. Sector-12 |  |
| 4 | Nilkhet | 1.68/3/B, Jhigatola, Dhaka |  |
|  |  | 2.Azimpur Collony |  |
|  |  | 3. BDR Gate No 1, Dhaka |  |
|  |  | 4.Bangabandhu Sheikh Mujibur Rahman Medical University |  |
|  |  | 5.Momotaj Plaza, Dhanmoni,Road No:04 |  |
|  |  | 6.Multiplan Centre, New Elephant Road |  |
| 5 | Motijheel | 1.Bangladesh Bank |  |
| 6 | Mirpur | 1.Tolar Bug, Mirpur |  |
|  |  | 2.Gabtoli/Mazar Road, Mirpur |  |
| 7 | Chakbazar | 1.Babu Bazar |  |
|  |  | 2.Midford Hospital |  |
|  |  | 3.Lalbag Chowrasta, Sheikh Shah Bazar, Dhaka. |  |
| 8 | Saidebad | 1. Konapara |  |
| 9 | Rampura | 1. Mohammadbag, Near Rajarbag |  |
|  |  | 2. Mahanagar Housing Society,Rampura(Near BTV) |  |

Annex 1.3

CAPACITY REQUIREMENT OF MDF PATCH PANEL

Patch Panel capacity

Site

Exchange side patch

Subscriber side patch

panel

panel

Requirement  Offered     Requirement    Offered

Type-A

Nandan Kanon,

Chittagong                       1000                                     1000

1

2  Central Sylhet,                  1000                                     1000

3  Central, Khulna                 1000                                     1000

1000                                 1000

4  Bogra

1000                                1000

5  Barisal

1000                                 1000

6  Rajshahi

1000                                1000

7  Gazipur

1000                                1000

8  Savar

9  Mymensingh                     1000                                     1000

1000                                1000

10  Jessore

Type-B

11  Chawkbazar, Dhaka          1500                                     1500

1500                               1500

12  Comilla

13  Sayedabad, Dhaka             1500                                     1500

14  Fakirapool, Dhaka             1500                                    1500

15  Narayangonj, Dhaka         1500                                     1500

16  Khilgaon, Dhaka               1500                                     1500

17  Cantonment, Dhaka           1500                                    1500

Type-C

18  Mirpur, Dhaka                   3000                                     3000

19  Nilkhet, Dhaka                  3000                                     3000

20  Agrabad, Chittagong         3000                                     3000

Type-D

21  Moghbazar, Dhaka            4000                                    4000

22  SBN, Dhaka                      4000                                     4000

23  Central, Dhaka                   4000                                    4000

24  Uttrara, Dhaka                   4000                                     4000

25  Gulshan, Dhaka                 4000                                     4000

Total

49500                                 49500

| Annex -1.4 |  |
| --- | --- |
| Capacity requirement of ODF |
|  |  | Present equipped capacity |  |  |
|  |  | Requirement | Bidder's offer |  |
| Type-A |  |
| 1 | Moghbazar, Dhaka | 24 |  |  |
| 2 | SBN, Dhaka | 24 |  |  |
| 3 | Chawkbazar, Dhaka | 24 |  |  |
| 3 | Comilla | 24 |  |  |
| 5 | Sayedabad, Dhaka | 24 |  |  |
| 6 | Mirpur, Dhaka | 24 |  |  |
| 7 | Narayangonj, Dhaka | 24 |  |  |
| 7 | Khilgaon, Dhaka | 24 |  |  |
| 9 | Cantonment, Dhaka | 24 |  |  |
| 10 | Agrabad, Chittagong | 24 |  |  |
| 11 | Nandan Kanon,Chittagong | 24 |  |  |
| 12 | Central Sylhet, | 24 |  |  |
| 13 | Central, Khulna | 24 |  |  |
| 14 | Bogra | 24 |  |  |
| 15 | Barisal | 24 |  |  |
| 16 | Rajshahi | 24 |  |  |
| 17 | Gazipur | 24 |  |  |
| 18 | Savar | 24 |  |  |
| 19 | Mymensingh | 24 |  |  |
| 20 | Jessore | 24 |  |  |
| Type-B |  |
| 21 | Gulshan, Dhaka | 48 |  |  |
| 22 | Central, Dhaka | 48 |  |  |
| 23 | Fakirapool, Dhaka | 48 |  |  |
| 24 | Secretariat, Dhaka | 48 |  |  |
| 25 | Nilkhet, Dhaka | 48 |  |  |
| 26 | Uttrara, Dhaka | 48 |  |  |

FORM A

SUMMARY PRICE OF THE BID

| SI | Name of Item | Total price |
| --- | --- | --- |
|  |  | USD + BD Taka |
| A | Total price for all equipment |
| 1 | Total price for all OLT (from all Form B.1) |  |  |
| 2 | Total price for all ONU (from all Form B.2) |  |  |
| 3 | Total price for MDF & ODF (from all Form B.3s) |  |  |
| 4 | Total price for all other equipment (from all Form B.4) |  |  |
| 5 | Total price for all OSP equipment (from all Form B.5) |  |  |
|  | Total price for equipment(FoB/FCA) |  |  |
| B | Total Freight (from all Bs) |  |  |
|  | Total price equipment (C&F) |  |  |
| x. | Total price for equipment (C&F) |  |  |
| D. | Total price for services |  |  |
| 1 | Total price for services of OLT (from all Form B.1) |  |  |
| 2 | Total price for services of ONU (from all Form B.2) |  |  |
| 3 | Total price for services of ODF & MDF (from all Form B.3) |  |  |
| 4 | Total price for services of other equipment (from all Form B.4s) |  |  |
| 5 | Total price for OSP services (from all Form B.5) |  |  |
| Y. | Total price for Service |  |  |
|  | Total price for the bid (X+Y) |  |  |
| In Words: US Dollar…………………………….plus BD Taka……………. …………………….only |

Form B.1

SUMMARY PRICE FOR OLT EQUIPMENT

(The Bidder shall fill up one form for each OLT site)

Total Price

Sl  Name of Item

USD + BD Taka

A      Total Price for Equipment (FoB/ FCA)

B       Total Freight

Total Price for Equipment (C&F)

C        Total Insurance

X.      Total Price for Equipment (CIF)

D       Total Price for Services

01.     Total Price for Installation Services

02.     Total Price for Testing/Commissioning

Services

Y.     Total Price for Services

Total Price for the OLT Equipment

In Words : US Dollar .....................................................................

and BD Taka .................. ................................................ only.

Form B.2

SUMMARY PRICE FOR ONU EQUIPMENT

Type of ONU:

(The Bidder shall fill up one form for each type of ONU)

Total Price

Sl     Name of Item

USD + BD Taka

A     Total Price for Equipment (FoB/ FCA)

B       Total Freight

Total Price for Equipment (C&F)

C      Total Insurance

X.      Total Price for Equipment (CIF)

D        Total Price for Services

01.     Total Price for Installation Services

02.     Total Price for Testing/Commissioning

Services

Y.       Total Price for Services

Total Price for the ONU (X+Y)

In Words : US Dollar .....................................................................

and BD Taka .................. ................................................ only.

Form B.3

SUMMARY PRICE FOR MDF

Type of the site :  ................................

(The Bidder shall fill up one form for each Type of MDF )

Total Price

Sl     Name of Item

USD + BD Taka

A       Price of Equipment

Price of MDF

Total Price for Equipment (FoB/ FCA)

B       Total Freight

Total Price for Equipment (C&F)

C       Total Insurance

X.      Total Price for Equipment (CIF)

D       Total Price for Services

01.     Total Price for Installation Services

02.     Total Price for Testing/Commissioning

Services

Y.     Total Price for Services

Total Price for MDF (X+Y)

In Words : US Dollar .....................................................................

and BD Taka .................. ................................................ only.

Form B.4

SUMMARY PRICE FOR ODF

Name of the site :  ................................

(The Bidder shall fill up one form for each Type of ODF )

Total Price

Sl     Name of Item

USD + BD Taka

A       Price of Equipment

Price of ODF

Total Price for Equipment (FoB/ FCA)

B       Total Freight

Total Price for Equipment (C&F)

C       Total Insurance

X.      Total Price for Equipment (CIF)

D       Total Price for Services

01.     Total Price for Installation Services

02.     Total Price for Testing/Commissioning

Services

Y.     Total Price for Services

Total Price for ODF (X+Y)

In Words : US Dollar .....................................................................

and BD Taka .................. ................................................ only.

Form B.5

SUMMARY PRICE FOR OTHER EQUIPMENT

Total Price

Sl

Name of Item

USD + BD Taka

A    Price for Related Equipment

01.  Price for Network Maintenance System (NMS)

02.  Price of any other item, if any

Sub - Total A

B     Price for Maintenance Spares for Buffer Stock (From

Form D)

Total Price for Other Equipment (A+B)

C     Total Freight

Total Price for Equipment (C&F)

D    Total Insurance

Total Price for Equipment (CIF) A+B+C+D

Form B.6

SUMMARY PRICE FOR OTHER SERVICES

Total Price

Sl

Name of Item

USD + BD

Taka

A     Total Price for Other Services related to Equipment

01.    Network Maintenance System (NMS)

02.   Other Service, if any

Sub-Total for A

B      Other services related to the whole system

01     Maintenance Support up to Performance Guarantee Period

02     Price for Performance Guarantee Period

03    CPOC

04    Local Training

05    Total Price for Provisional Acceptance Test

06    Total Price for Final Acceptance Test

Sub - Total for B

C     Total Price for Other Services related to Turn-Key completion of the Project

01.    Total Price for 7 years maintenance service after FAT

02.   Total Price for Inter-working/Connection Services

Sub - Total for C

Total for Other Services (A + B+C)

Form B.7

SUMMARY PRICE FOR OSP

Total Cost

Sl. No.  Name of Items  Unit

Quantity

FOB

Level

USD

BDT

(FOB)

Out Side Plant

1.        Material Supply

1.1       Material – OF Cable

1         Optical Fibre Cable (24 fibre) in-station.        Meter        1000

2        Optical Fibre Cable (24fibre) for duct and

Meter     120000

Direct buried installation.

Meter      10000

3        Spares for OF Cable (24 fibre) for duct and

direct buried installation

Sub-Total

1.2       Material – Pipe and Accessories

Meter     25000

1        1x40/33 mm (wall thickness 3.5 mm) HDPE

Duct/Sub-duct with permanent solid

Lubrication inside

Meter    60000

3        110 mm (outer dia) and 3.2 mm (wall

Thickness PVC Duct (in Taka)

Meter     200

4        100mm (Inner Dia.) and 3 mm (wall

Thickness) perforated GI Pipe. (in Taka)

Pc          50

5        Push Fit HDPE Pipe Coupler.

Pc          50

6        GI-PVC Coupler.(in Taka)

Sub-Total

1.3       Material - Manhole Accessories

Pc           5

1         Manhole Cover & Frame

Pc           5

2        Sump Pit Cover

Pc           5

3         Manhole Ladder. (in Taka)

4        Pulling Hook (Pulling in iron) (in Taka)               Pc          20

5        Bell Mouth. (in Taka)

Pc         40

6        Rubber End Cap (with and w/o hole) (in Taka)     Pc         40

7        Hook-Bolt and Nut (6 nos per set) (in Taka)         Set       100

8        Cable Rack and Bracket (3 vertical and 3

Set         10

horizontal part per Set) (in Taka)

Sub-Total

1.4       Material - Handhole Accessories

Pc         10

1        Concrete Post. (in Taka)

Pc         10

2        Bell Mouth (in Taka)

3         Rubber End Cap (with and w/o hole) (in Taka)         Pc          10

Sub-Total

1.5       Material – Other Accessories

1        Warning Tape 5 cm X 0.15 mm                           Meter   10000

2        Marker Tag

Pc        20

Total Cost

Sl. No.  Name of Items  Unit

Quantity

FOB

Level

USD

BDT

(FOB)

Sub-Total

1.6       Material – Consumables during Installation

1         Drawing Rope (Nylon) (in Taka)                          Meter     10000

1.7        Material - OF Jointing and Termination Kits

Each      10

1        24 fiber Optical joint closures equipped with

required splice tray, splice protector.

10

2        Spare 24 fiber Optical joint closure equipped

with required splice tray, splice protector.

Each     12

3        Optical Fiber Distribution / Termination box

equipped with 18 Pigtail (3 m), 18 U-Link, 18

Patch cord (5 m) along with necessary splice

tray and splice protector

Each     100

4        Spare Pigtail (3 m)

Each     100

5        Spare Patchcord (5 m)

Each     100

6        Spare Patchcord (10 m)

Sub-Total

A. Total of Materials

2.        Services (in Taka)

2.1       Service – Duct Installation

Meter 5000

1  4    way 110mm PVC Duct Installation 1.2 ± 0.1

m deep Trenching, Laying of 4 nos of 110mm

dia PVC Pipes with necessary Spacer at each 2

m with 10 cm Sand bed below and above the

Pipes, Installation of Cement Concrete Slab

protection (50cm x 30cm x 5cm), Warning Tape

(5 cm X 0.15 mm) and back filled with

excavated soil and compaction. (Price includes

supply of all construction material, slab, sand

and breaking of any surface).

Meter 20000

2  2    way 110mm PVC Duct Installation 1.2 ± 0.1

m deep Trenching, Laying of 4 nos of 110mm

dia PVC Pipes with necessary Spacer at each 2

m with 10 cm Sand bed below and above the

Pipes, Installation of Cement Concrete Slab

protection (50cm x 30cm x 5cm), Warning Tape

(5 cm X 0.15 mm) and back filled with

excavated soil and compaction. (Price includes

supply of all construction material, slab, sand

and breaking of any surface).

Meter 50

4  1     way GI Pipe Duct at Bridge and Culvert

Crossing

Perforation of 4” (Inner Die), 3 mm (Thickness)

GI Pipe and Installation of 1 no GI pipe along

bridge and Culvert using Galvanised clamps at

each 1 m distance and bending of pipes up to 1.2

Total Cost

Sl. No.  Name of Items  Unit

Quantity

FOB

Level

USD

BDT

(FOB)

± 0.1 m depth from ground level and

termination with GI-PVC coupler.

Meter  10

5        1 WAY Rail boring

Boring of Railway line and Installation of 1x4”

(Inner Dia), 3 mm (Thickness) GI Pipe 1.2 ± 0.1

m depth from ground level and termination with

GI-PVC coupler.

2.2      Service – Other Duct and Cable related

Installation work

Meter 45000

1        HDPE Sub-Duct installation in Main PVC /

GI Duct

Installation of 1 no of 40/33 mm HDPE sub-

duct in one PVC / GI duct all through the route

Meter 65000

2        HDPE Sub-Duct installation in partially

filled primary PVC / GI Duct

Installation of 1 no. of 40/33 mm HDPE sub-

duct in one partially filled primary PVC / GI

duct.

Meter 10000

3        HDPE Sub-Duct installation Direct Burried

Installation of 1 no. of 40/33 mm HDPE sub-

duct in one partially filled primary PVC / GI

duct.

Meter 120000

3        FO Cable installation in HDPE Duct/Sub-

duct

Installation of 18 Fiber Cable in HDPE

New/Old Duct/Sub-duct all through the route

(i.e. 4way PVC, 4 way GI, 2 way HDPE, 1 way

GI and 1 way HDPE duct area.

Meter 200

4        In Station FO Cable installation (Through

New Cable Tray)

Installation of 12/18/24 Fiber In Station Cable

providing 300 mm cable tray with necessary

fitting and fixing.

Meter 200

5.        In Station FO Cable installation (Through

Existing Cable Tray)

Installation of 12/18/24 Fiber In Station Cable

using existing Cable tray providing necessary

fitting and fixing.

2.3      Service – Manhole and Handhole related

Installation work

Each   5

1  S-2 Type Manhole

Excavations, Construction of S-2 Type

Manholes complete with all civil construction

materials. Manhole sides and necessary back

filling with excavated soil. Including neck

making, fixing of Hardware (i.e. cable rack,

Total Cost

Sl. No.  Name of Items  Unit

Quantity

FOB

Level

USD

BDT

(FOB)

bracket, Ladder, sum pit cover, pulling in iron,

Bell mouth, marker tag and fixing of cover).

Each   10

2         Construction of reinforced Concrete Hand Holes

Excavation and Construction of reinforced

concrete handhole complete with all civil

construction materials including fixing of

Bellmouth, Marker tag, and concrete post.

Handhole sides and necessary back filling with

excavated soil. Price includes handhole cover (4

Piece cover construction) and will be

constructed and placed 0.5m below surface

2.4       Service – Jointing and Termination

Each    28

1         Jointing of 24 Fiber Cable

Cutting, Cleaning, Preparing and

Splicing/jointing of 18 Fiber cable in Joint

Closure and proper placing the Joint closure

inside Manhole / Handhole

Each   28

2        Fiber Termination of 24 Fiber Cable

Cutting, Cleaning, Preparing and

Termination of existing 18 Fiber cable in

Fiber Termination Box.

B. Total of Services

Grand Total (A+B)

Form C.1

Detail BoQ for OLT

(The Bidder shall fill up one form for each site)

Unit Price  Total Price

Sl  Name of Item  Quantity

USD  +     BD

USD  +      BD

Taka

Taka

A   Price for OLT Equipment

The Bidder shall show the detail BoQ as per his

choice and shall satisfy all requirements specified in

this tender document

Sub-Total for OLT Equipment

B    Price for Services

01  Installation Services

02 Testing/Commissioning Services

Sub - Total for Services

Total for OLT System A+B

Form C.2

Detail BoQ for ONU

(The Bidder shall fill up one form for each type of ONU)

Unit Price     Total Price

Sl  Name of Item  Quantity

USD   +     BD

USD +   BD

Taka

Taka

A   Price for ONU Equipment

The Bidder shall show the detail BoQ as per his

choice and shall satisfy all requirements specified in

this tender document

Sub-Total for ONU Equipment

B    Price for Services

01   Installation Services

02  Testing/Commissioning Services

Sub - Total for Services

Total for ONU System A+B

Form C.3

Detail BoQ for MDF

(The Bidder shall fill up one form for each type of MDF)

Unit Price  Total Price

Sl   Name of Item  Quantity

USD  +     BD

USD  +     BD

Taka

Taka

A  Price for MDF Equipment

The Bidder shall show detail BOQ as per his choice and shall

satisfy all requirements specified in the tender document

Sub-Total for MDF Equipment

B    Price for Services

01  Installation Services

02  Testing/Commissioning Services

Sub - Total for Services

Total for MDF System A+B

Form C.4

Detail BoQ for ODF

(The Bidder shall fill up one form for each type of ODF)

Unit Price              Total Price

Sl  Name of Item  Quantity

USD  +     BD

USD  +        BD

Taka

Taka

A    Price for ODF Equipment

The Bidder shall show the detail BoQ as per his

choice and shall satisfy all requirements specified

in this tender document

Sub-Total for ODF Equipment

B  Price for Services

01      Installation Services

02      Testing/Commissioning Services

Sub - Total for Services

Total for ODF System A+B

Form C.5

DETAIL BOQ FOR OTHER EQUIPMENT

Unit Price            Total Price

Sl    Name of Item  Quantity

USD   +       BD

USD  +         BD

Taka

Taka

A  Price for Network Maintenance

System (NMS)

The Bidder shall show the detail BoQ as per his

choice and shall satisfy all requirements specified in this tnder document

Sub - Total for NMS

B       200 km 0.4 mm tip cable

C       Price for Other Equipment not

mentioned in any Form but

necessary for proper

implementation of the work

The Bidder shall show the detail BoQ as per his

choice and shall satisfy all requirements specified in

this tender document

Sub - Total for Other Equipment

Total for other Equipment

Form C.6

DETAIL BOQ FOR OTHER SERVICES

Unit Price            Total Price

Sl    Name of Item  Quantity

USD +    BD

USD  +       BD

Taka

Taka

A     Other Services related to specific Equipment

The Bidder shall show the detail BoQ as per

his choice and shall satisfy all requirements

specified in this tender document

01   Network Maintenance System (NMS)

Sub-Total for A

B    Other services related to the whole system

The Bidder shall show the detail BoQ as per

his choice and shall satisfy all requirements

specified in this tender document

01    Maintenance Support up to

Performance Guarantee Period

02    Price for Performance Guarantee

Period

03    Local Training

04   Total Price for Provisional Acceptance

Test

05   Total Price for Final Acceptance Test

06

07

Sub - Total for B

C  Other Services related to Turn-Key completion of the Project

The Bidder shall show the detail BoQ as per

his choice and shall satisfy all requirements

sp ecified in this tender document

01   Total price for seven years

maintenance service after FAT

02   Total Price for Inter-

working/Connection Services

Sub - Total for C

Total for Other Services (A + B+C)

Form D

DETAIL BOQ FOR MAINTENANCE SPARES FOR BUFFER STOCK

Unit Price      Total Price

Sl    Name of Item  Quantity

USD +    BD

USD  +       BD

Taka

Taka

The Bidder shall show the detail BoQ as per his choice

and shall satisfy all requirements specified in this tender

document

Total for Maintenance Spares for

Buffer Stock

Form E

QUOTATION FOR FUTURE ORDER

(a) Future Order Formula for Equipment:

(b) Future Order Formula for Service:

Form F

SUMMARY OF THE BID EQUIPMENT

Sl                   Name of Item

Model

Number

& Name

Manufac-

turer's

Name

Manufac-

turer's

Address

Country

of Origin

A        Main Equipment

a         OLT

b         ONU

c         Optical Fiber cables

d         MDF Patch panel

e         ODF

a Server

b Software

B  Network Maintenance System (NMS)

# Text boxes

‡Uwj‡dvb wkí ms¯’v wjwg‡UW

Phone: 9814747, FAX: 880-2-9812700, Web Site: www.tss.com.bd

E-mail: mdtss@btel.net.bd / info@tss.com.bd